; ****************************************************************
; Displays patterns on an 8x8 LED Matrix that uses the MAX7219
; serial data LED driver.
;
; Randomly determines whether to display a beating heart or
; the zombie display (X).
;
; Assumes that we are using the default 4-MHz internal clock.
;
; All routines will exit pointing to bank0.
; ****************************************************************
;
        LIST P=PIC12F683
        #INCLUDE <p12f683.inc>

        ERRORLEVEL 0, -302 ;suppress bank selection messages

        __CONFIG _FOSC_INTOSCIO & _WDT_OFF & _PWRTE_ON & _MCLRE_OFF & _BOD_OFF & _CPD_OFF & _CP_OFF

; Control lines
#define S_Data GPIO,0 ;LED Serial Data
#define Clock GPIO,4 ;LED Clock
#define C_S GPIO,2 ;LED Chip Select
#define S_Data_T TRISIO,0
#define Clock_T TRISIO,4
#define C_S_T TRISIO,2

;Touch module analog input
#define Touch GPIO,1 ;Finger touch (comparator C- input)

;LED register address defines
#define No_Op 0x00 ;No Operation
#define Dig0 0x01 ;Digit 0 (column 0)
#define Dig1 0x02 ;Digit 1 (column 1)
#define Dig2 0x03 ;Digit 2 (column 2)
#define Dig3 0x04 ;Digit 3 (column 3)
#define Dig4 0x05 ;Digit 4 (column 4)
#define Dig5 0x06 ;Digit 5 (column 5)
#define Dig6 0x07 ;Digit 6 (column 6)
#define Dig7 0x08 ;Digit 7 (column 7)
#define Decode 0x09 ;Decode Mode
#define Brite 0x0A ;Brightness
#define Scan 0x0B ;Scan Limit
#define Switch 0x0C ;0=off, 1=on
#define Disp_Tst 0x0F ;Display Test

        UDATA 0x20
Data_Byte RES 1 ;Data for transmission
Delay_Cnt RES 1 ;Delay counter
Bit_Cnt RES 1 ;Bit counter for serial output

;----------------------------------------------------
; Program code starts here
;----------------------------------------------------

RESET CODE 0x00
        GOTO Init

Int_Vec CODE 0x04
        RETFIE

;------------------------------------------------------------------------------
Init NOP
        BANKSEL TRISIO ;bank1
        BCF S_Data_T ;output
        BCF Clock_T ;output
        BCF C_S_T ;output
        CLRF ANSEL ;set ports as digital I/O (12F683)
        BSF ANSEL, 1 ;GPIO1: analog input
        MOVLW b'10001111' ;Vref = (Vdd/4) + (15/32 * Vdd)
        MOVWF VRCON
        MOVLW 0x87
        MOVWF OPTION_REG ;Timer0 internal clock, prescale = 256

        BANKSEL GPIO ;bank0
        MOVLW b'00000100' ;C- input only, internal Vref
        MOVWF CMCON0 ;turn on comparator
        CALL Delay400ms ;give LED time to power on
        CALL Init_LED
        CALL Delay400ms

Main_Loop CALL LEDs_Off
        CALL Delay400ms
        BTFSC CMCON0, COUT
        GOTO Main_Loop
        MOVFW TMR0
        SUBLW d'100'
        BTFSC STATUS, C
        GOTO main3
main1 CALL Heart
        CALL Delay400ms
main2 CALL LEDs_Off
        CALL Delay200ms
        CALL LEDs_On
        CALL Delay400ms
        BTFSC CMCON0, COUT
        GOTO Main_Loop
        GOTO main2
main3 CALL Zombie
main4 BTFSC CMCON0, COUT
        GOTO Main_Loop
        GOTO main4

Heart MOVLW Dig0
        CALL Send_Addr
        MOVLW b'01110000'
        CALL Send_Data
        MOVLW Dig1
        CALL Send_Addr
        MOVLW b'11111000'
        CALL Send_Data
        MOVLW Dig2
        CALL Send_Addr
        MOVLW b'11111100'
        CALL Send_Data
        MOVLW Dig3
        CALL Send_Addr
        MOVLW b'01111110'
        CALL Send_Data
        MOVLW Dig4
        CALL Send_Addr
        MOVLW b'01111110'
        CALL Send_Data
        MOVLW Dig5
        CALL Send_Addr
        MOVLW b'11111100'
        CALL Send_Data
        MOVLW Dig6
        CALL Send_Addr
        MOVLW b'11111000'
        CALL Send_Data
        MOVLW Dig7
        CALL Send_Addr
        MOVLW b'01110000'
        CALL Send_Data
        CALL LEDs_On
        RETURN

Zombie MOVLW Dig0
        CALL Send_Addr
        MOVLW b'10000001'
        CALL Send_Data
        MOVLW Dig1
        CALL Send_Addr
        MOVLW b'01000010'
        CALL Send_Data
        MOVLW Dig2
        CALL Send_Addr
        MOVLW b'00100100'
        CALL Send_Data
        MOVLW Dig3
        CALL Send_Addr
        MOVLW b'00011000'
        CALL Send_Data
        MOVLW Dig4
        CALL Send_Addr
        MOVLW b'00011000'
        CALL Send_Data
        MOVLW Dig5
        CALL Send_Addr
        MOVLW b'00100100'
        CALL Send_Data
        MOVLW Dig6
        CALL Send_Addr
        MOVLW b'01000010'
        CALL Send_Data
        MOVLW Dig7
        CALL Send_Addr
        MOVLW b'10000001'
        CALL Send_Data
        CALL LEDs_On
        RETURN

Init_LED MOVLW Decode
        CALL Send_Addr
        MOVLW 0x00 ;turn off BCD mode
        CALL Send_Data
        MOVLW Scan
        CALL Send_Addr
        MOVLW d'7' ;Scan limit (0-7)
        CALL Send_Data
        MOVLW Brite
        CALL Send_Addr
        MOVLW d'3' ;Brightness (0-15)
        CALL Send_Data
        RETURN

Clear_LED MOVLW Dig0
        CALL Send_Addr
        MOVLW 0x00
        CALL Send_Data
        MOVLW Dig1
        CALL Send_Addr
        MOVLW 0x00
        CALL Send_Data
        MOVLW Dig2
        CALL Send_Addr
        MOVLW 0x00
        CALL Send_Data
        MOVLW Dig3
        CALL Send_Addr
        MOVLW 0x00
        CALL Send_Data
        MOVLW Dig4
        CALL Send_Addr
        MOVLW 0x00
        CALL Send_Data
        MOVLW Dig5
        CALL Send_Addr
        MOVLW 0x00
        CALL Send_Data
        MOVLW Dig6
        CALL Send_Addr
        MOVLW 0x00
        CALL Send_Data
        MOVLW Dig7
        CALL Send_Addr
        MOVLW 0x00
        CALL Send_Data
        RETURN

LEDs_On MOVLW Switch
        CALL Send_Addr
        MOVLW d'1' ;Switch matrix on
        CALL Send_Data
        RETURN

LEDs_Off MOVLW Switch
        CALL Send_Addr
        MOVLW d'0' ;Switch matrix off
        CALL Send_Data
        RETURN

;------------------------------------------------------------------------------
; These routines assume that the data to send is in W.
;------------------------------------------------------------------------------

Send_Addr MOVWF Data_Byte ;Send what's in W
        MOVLW 0x08 ;8 bits to send
        MOVWF Bit_Cnt
addr_loop RLF Data_Byte, F ;MSB sent first
        BTFSS STATUS, C ;Test the carry bit
        BCF S_Data ;Set data bit to '0'
        BTFSC STATUS, C ;Test the carry bit
        BSF S_Data ;Set data bit to a '1'
        BSF Clock ;shift reg clocks on rising edge
        BCF Clock
        DECFSZ Bit_Cnt,F
        GOTO addr_loop
        RETURN

Send_Data CALL Send_Addr
        CALL Delay1ms
        BSF C_S ;latch data
        BCF C_S
        RETURN

;-----------------------------------
; Delay routines (4-MHz clock)
;-----------------------------------

Delay1ms MOVLW d'249'
        GOTO Cntdwn

Delay100ms MOVLW d'100'
        MOVWF Delay_Cnt
loop100ms CALL Delay1ms
        DECFSZ Delay_Cnt, F
        GOTO loop100ms
        RETURN

Delay200ms CALL Delay100ms
        GOTO Delay100ms

Delay400ms CALL Delay200ms
        GOTO Delay200ms

Cntdwn ADDLW -1 ;decrement W
        BTFSS STATUS, Z ;Zero flag set?
        GOTO Cntdwn ;No, keep looping
        RETURN ;Yes, timeout done

; ------------------------------------------------------------------------------

        END