; ****************************************************************
; ESP8266 wifi module interface to control Etekcity RF sockets.
; Commands are received from a webpage and then translated into
; hex code strings that are sent to an RF transmitter module.
; The output to the transmitter module is via a single I/O pin.
;
; Set up to control 5 outlets. Outlets 4 and 5 have been hacked
; to be normally on at power up instead of normally off so their
; "On/Off" commands are swapped.
;
; Uses the serial port of the PIC to send and receive AT commands
; to the ESP8266 module.
;
; Serial port communications are at the 9600 baud.
;
; Polling of the serial receive interrupt flag is used instead of
; an actual interrupt for this simple routine.
;
; Receiver overflows are expected because the ESP8266 echos the
; command strings.
;
; Assumes that we are using the 8-MHz internal clock.
;
; All routines will exit pointing to bank0.
; ****************************************************************
;
        LIST P=PIC16F1847
        #INCLUDE <p16f1847.inc>

        ERRORLEVEL	0,	-302	;suppress bank selection messages

        __CONFIG _CONFIG1, _FOSC_INTOSC & _WDTE_OFF & _PWRTE_ON & _MCLRE_OFF & _BOREN_OFF & _CPD_OFF & _CP_OFF
        __CONFIG _CONFIG2, _LVP_OFF & _PLLEN_OFF

; Port defines
#define Serial_RF PORTA, 1 ;Serial output to RF module
#define Serial_RF_T TRISA, 1 ;Serial output to RF module

RAM0 UDATA 0x20 ;Bank0 RAM (80 bytes maximum)
Data_Byte RES 1 ;Data for transmission
DelayCount RES 1 ;Delay Counter
BitCount RES 1 ;Counter
Dummy RES 1 ;dummy variable
RF_Byte1 RES 1 ;RF Command, byte 1
RF_Byte2 RES 1 ;RF Command, byte 2
RF_Byte3 RES 1 ;RF Command, byte 3
Web_Cmd RES 1 ;command from the webpage
Char_Cnt_U RES 1 ;character count (units digit)
Char_Cnt_T RES 1 ;character count (tens digit)
Char_Cnt_H RES 1 ;character count (hundreds digit)
Msg_Ptr_L1 RES 1 ;message pointer 1 (low)
Msg_Ptr_H1 RES 1 ;message pointer 1 (high)
Msg_Ptr_L2 RES 1 ;message pointer 2 (low)
Msg_Ptr_H2 RES 1 ;message pointer 2 (high)
Socket1 RES 1 ;Etekcity socket 1
Socket2 RES 1 ;Etekcity socket 2
Socket3 RES 1 ;Etekcity socket 3
Socket4 RES 1 ;Etekcity socket 4
Socket5 RES 1 ;Etekcity socket 5

;-----------------------------------
; Program code starts here
;-----------------------------------

Pwr_On CODE 0x00
        GOTO Init

Int_Vec CODE 0x04
        RETFIE

Init NOP ;error if go directly to BANKSEL
        BANKSEL TRISA ;bank1
        MOVLW 0x70 ;8-MHz internal clock
        MOVWF OSCCON
        BCF Serial_RF_T ;set as output
        BANKSEL ANSELA ;bank3
        CLRF ANSELA ;all digital
        CLRF ANSELB ;all digital
        BANKSEL PORTA ;bank0
        CLRF PORTA
        MOVLW 0x02 ;Init socket status to unknown
        MOVWF Socket1
        MOVWF Socket2
        MOVWF Socket3
        MOVWF Socket4
        MOVWF Socket5
        CALL Init_Serial
        CALL Wait_ESP ;wait for ESP8266 to init
        CALL Server_On

Main_Loop CALL Wait_IPD ;wait for request from webpage
        CALL Wait_Cmd ;wait for command number
        CALL Send_Data ;send data to the webpage
        GOTO Main_Loop

Wait_ESP CALL RX_Serial
        SUBLW 'G'
        BTFSS STATUS, Z
        GOTO Wait_ESP
        CALL RX_Serial
        SUBLW 'O'
        BTFSS STATUS, Z
        GOTO Wait_ESP
        CALL RX_Serial
        SUBLW 'T'
        BTFSS STATUS, Z
        GOTO Wait_ESP
        CALL RX_Serial
        SUBLW ' '
        BTFSS STATUS, Z
        GOTO Wait_ESP
        CALL RX_Serial
        SUBLW 'I'
        BTFSS STATUS, Z
        GOTO Wait_ESP
        CALL RX_Serial
        SUBLW 'P'
        BTFSS STATUS, Z
        GOTO Wait_ESP
        RETURN

Server_On MOVLW LOW Command1 ;low 8 bits of table address
        MOVWF FSR0L
        MOVLW HIGH Command1 ;high 8 bits of table address
        MOVWF FSR0H
        CALL Send_Char ;CIPMUX
        CALL Wait_OK
        MOVLW LOW Command2 ;low 8 bits of table address
        MOVWF FSR0L
        MOVLW HIGH Command2 ;high 8 bits of table address
        MOVWF FSR0H
        CALL Send_Char ;CIPSERVER
        CALL Wait_OK
        RETURN

Wait_OK CALL RX_Serial
        SUBLW 'O'
        BTFSS STATUS, Z
        GOTO Wait_OK
        CALL RX_Serial
        SUBLW 'K'
        BTFSS STATUS, Z
        GOTO Wait_OK
        RETURN

Wait_IPD CALL RX_Serial
        SUBLW '+'
        BTFSS STATUS, Z
        GOTO Wait_IPD
        CALL RX_Serial
        SUBLW 'I'
        BTFSS STATUS, Z
        GOTO Wait_IPD
        CALL RX_Serial
        SUBLW 'P'
        BTFSS STATUS, Z
        GOTO Wait_IPD
        CALL RX_Serial
        SUBLW 'D'
        BTFSS STATUS, Z
        GOTO Wait_IPD
        CALL RX_Serial
        SUBLW ','
        BTFSS STATUS, Z
        GOTO Wait_IPD
        CALL RX_Serial
        SUBLW '0'
        BTFSS STATUS, Z
        GOTO Wait_IPD
        RETURN

Wait_Cmd MOVLW d'3' ;wait for three consecutive Q characters
        MOVWF Dummy
Wait_Cmd1 CALL RX_Serial
        SUBLW 'Q'
        BTFSS STATUS, Z
        GOTO Wait_Cmd
        DECFSZ Dummy, F
        GOTO Wait_Cmd1 ;waiting for more Q characters
        CALL RX_Serial ;get command number
        MOVWF Web_Cmd
        RETURN

Send_Data MOVLW LOW Command3 ;low 8 bits of table address
        MOVWF FSR0L
        MOVLW HIGH Command3 ;high 8 bits of table address
        MOVWF FSR0H
        CALL Send_Char ;CIPSEND
        CALL Parse_Cmd ;parse, execute, and reply to the command
        CALL Wait_OK
        MOVLW LOW Command4 ;low 8 bits of table address
        MOVWF FSR0L
        MOVLW HIGH Command4 ;high 8 bits of table address
        MOVWF FSR0H
        CALL Send_Char ;CIPCLOSE
        CALL Wait_OK
        RETURN

Parse_Cmd NOP
        BANKSEL PORTA ;bank0
        MOVFW Web_Cmd
        SUBLW '1'
        BTFSC STATUS, Z
        GOTO Do_Cmd1
        MOVFW Web_Cmd
        SUBLW '2'
        BTFSC STATUS, Z
        GOTO Do_Cmd2
        MOVFW Web_Cmd
        SUBLW '3'
        BTFSC STATUS, Z
        GOTO Do_Cmd3
        MOVFW Web_Cmd
        SUBLW '4'
        BTFSC STATUS, Z
        GOTO Do_Cmd4
        MOVFW Web_Cmd
        SUBLW '5'
        BTFSC STATUS, Z
        GOTO Do_Cmd5
        MOVFW Web_Cmd
        SUBLW '6'
        BTFSC STATUS, Z
        GOTO Do_Cmd6
        MOVFW Web_Cmd
        SUBLW '7'
        BTFSC STATUS, Z
        GOTO Do_Cmd7
        MOVFW Web_Cmd
        SUBLW '8'
        BTFSC STATUS, Z
        GOTO Do_Cmd8
        MOVFW Web_Cmd
        SUBLW '9'
        BTFSC STATUS, Z
        GOTO Do_Cmd9
        MOVFW Web_Cmd
        SUBLW '0'
        BTFSC STATUS, Z
        GOTO Do_Cmd0
        GOTO Bad_Cmd

;Turn on Socket 1
Do_Cmd1 MOVLW 0x01
        MOVWF Socket1
        MOVLW 0x44
        MOVWF RF_Byte1
        MOVLW 0x15
        MOVWF RF_Byte2
        MOVLW 0x33
        MOVWF RF_Byte3
        CALL Output_RF
        GOTO Do_Status

;Turn on Socket 2
Do_Cmd2 MOVLW 0x01
        MOVWF Socket2
        MOVLW 0x44
        MOVWF RF_Byte1
        MOVLW 0x15
        MOVWF RF_Byte2
        MOVLW 0xC3
        MOVWF RF_Byte3
        CALL Output_RF
        GOTO Do_Status

;Turn on Socket 3
Do_Cmd3 MOVLW 0x01
        MOVWF Socket3
        MOVLW 0x44
        MOVWF RF_Byte1
        MOVLW 0x17
        MOVWF RF_Byte2
        MOVLW 0x03
        MOVWF RF_Byte3
        CALL Output_RF
        GOTO Do_Status

;Turn on Socket 4 (Use "off" command)
Do_Cmd4 MOVLW 0x01
        MOVWF Socket4
        MOVLW 0x44
        MOVWF RF_Byte1
        MOVLW 0x1D
        MOVWF RF_Byte2
        MOVLW 0x0C
        MOVWF RF_Byte3
        CALL Output_RF
        GOTO Do_Status

;Turn on Socket 5 (use "Off" command)
Do_Cmd5 MOVLW 0x01
        MOVWF Socket5
        MOVLW 0x44
        MOVWF RF_Byte1
        MOVLW 0x35
        MOVWF RF_Byte2
        MOVLW 0x0C
        MOVWF RF_Byte3
        CALL Output_RF
        GOTO Do_Status

;Turn off Socket 1
Do_Cmd6 CLRF Socket1
        MOVLW 0x44
        MOVWF RF_Byte1
        MOVLW 0x15
        MOVWF RF_Byte2
        MOVLW 0x3C
        MOVWF RF_Byte3
        CALL Output_RF
        GOTO Do_Status

;Turn off Socket 2
Do_Cmd7 CLRF Socket2
        MOVLW 0x44
        MOVWF RF_Byte1
        MOVLW 0x15
        MOVWF RF_Byte2
        MOVLW 0xCC
        MOVWF RF_Byte3
        CALL Output_RF
        GOTO Do_Status

;Turn off Socket 3
Do_Cmd8 CLRF Socket3
        MOVLW 0x44
        MOVWF RF_Byte1
        MOVLW 0x17
        MOVWF RF_Byte2
        MOVLW 0x0C
        MOVWF RF_Byte3
        CALL Output_RF
        GOTO Do_Status

;Turn off Socket 4 (use "On" command)
Do_Cmd9 CLRF Socket4
        MOVLW 0x44
        MOVWF RF_Byte1
        MOVLW 0x1D
        MOVWF RF_Byte2
        MOVLW 0x03
        MOVWF RF_Byte3
        CALL Output_RF
        GOTO Do_Status

;Turn off Socket 5 (use "On" command)
Do_Cmd0 CLRF Socket5
        MOVLW 0x44
        MOVWF RF_Byte1
        MOVLW 0x35
        MOVWF RF_Byte2
        MOVLW 0x03
        MOVWF RF_Byte3
        CALL Output_RF
        GOTO Do_Status

;-------------------------------------------------
; Send status of outputs
;-------------------------------------------------
Do_Status MOVLW d'9'
        MOVWF Char_Cnt_U
        MOVLW d'7'
        MOVWF Char_Cnt_T
        MOVLW d'3'
        MOVWF Char_Cnt_H
        CALL End_Cmd

Do_Open MOVLW LOW HTML_Open ;low 8 bits of table address
        MOVWF FSR0L
        MOVLW HIGH HTML_Open ;high 8 bits of table address
        MOVWF FSR0H
        CALL Send_Char

Do_Msg1 CALL Msg_Start
        MOVLW LOW Message1 ;low 8 bits of table address
        MOVWF FSR0L
        MOVLW HIGH Message1 ;high 8 bits of table address
        MOVWF FSR0H
        CALL Send_Char
        MOVFW Socket1
        CALL Send_Color

Do_Msg2 CALL Msg_Start
        MOVLW LOW Message2 ;low 8 bits of table address
        MOVWF FSR0L
        MOVLW HIGH Message2 ;high 8 bits of table address
        MOVWF FSR0H
        CALL Send_Char
        MOVFW Socket2
        CALL Send_Color

Do_Msg3 CALL Msg_Start
        MOVLW LOW Message3 ;low 8 bits of table address
        MOVWF FSR0L
        MOVLW HIGH Message3 ;high 8 bits of table address
        MOVWF FSR0H
        CALL Send_Char
        MOVFW Socket3
        CALL Send_Color

Do_Msg4 CALL Msg_Start
        MOVLW LOW Message4 ;low 8 bits of table address
        MOVWF FSR0L
        MOVLW HIGH Message4 ;high 8 bits of table address
        MOVWF FSR0H
        CALL Send_Char
        MOVFW Socket4
        CALL Send_Color

Do_Msg5 CALL Msg_Start
        MOVLW LOW Message5 ;low 8 bits of table address
        MOVWF FSR0L
        MOVLW HIGH Message5 ;high 8 bits of table address
        MOVWF FSR0H
        CALL Send_Char
        MOVFW Socket5
        CALL Send_Color
        GOTO Do_Close

Msg_Start MOVLW LOW Msg_Begin ;low 8 bits of table address
        MOVWF FSR0L
        MOVLW HIGH Msg_Begin ;high 8 bits of table address
        MOVWF FSR0H
        CALL Send_Char
        RETURN

Send_Color MOVWF Dummy
        BTFSC STATUS, Z
        GOTO Out_Off
        BTFSC Dummy, 1
        GOTO Out_Unk
        BTFSC Dummy, 0
        GOTO Out_On

;Outlet Unknown status
Out_Unk MOVLW LOW Msg_White ;low 8 bits of table address
        MOVWF FSR0L
        MOVLW HIGH Msg_White ;high 8 bits of table address
        MOVWF FSR0H
        CALL Send_Char
        RETURN

;Outlet On status
Out_On MOVLW LOW Msg_Green ;low 8 bits of table address
        MOVWF FSR0L
        MOVLW HIGH Msg_Green ;high 8 bits of table address
        MOVWF FSR0H
        CALL Send_Char
        RETURN

;Outlet Off status
Out_Off MOVLW LOW Msg_Red ;low 8 bits of table address
        MOVWF FSR0L
        MOVLW HIGH Msg_Red ;high 8 bits of table address
        MOVWF FSR0H
        CALL Send_Char
        RETURN

Do_Close MOVLW LOW HTML_Close ;low 8 bits of table address
        MOVWF FSR0L
        MOVLW HIGH HTML_Close ;high 8 bits of table address
        MOVWF FSR0H
        CALL Send_Char
        RETURN

Bad_Cmd MOVLW d'11'
        MOVWF Char_Cnt_U
        CLRF Char_Cnt_T
        CLRF Char_Cnt_H
        CALL End_Cmd
        MOVLW LOW Bad_Msg ;low 8 bits of table address
        MOVWF FSR0L
        MOVLW HIGH Bad_Msg ;high 8 bits of table address
        MOVWF FSR0H
        CALL Send_Char ;send response
        RETURN

;-------------------------------------------------
; This routine completes the CIPSEND command
;-------------------------------------------------
End_Cmd MOVFW Char_Cnt_H
        IORLW 0x30 ;convert to ASCII
        CALL TX_Serial
        MOVFW Char_Cnt_T
        IORLW 0x30 ;convert to ASCII
        CALL TX_Serial
        MOVFW Char_Cnt_U
        IORLW 0x30 ;convert to ASCII
        CALL TX_Serial
        MOVLW 0x0D ;carriage return
        CALL TX_Serial
        MOVLW 0x0A ;line feed
        CALL TX_Serial
        CALL Wait_OK
        RETURN

;-------------------------------------------------
; Send characters to the ESP8266
;-------------------------------------------------
Send_Char NOP
        MOVIW 0[FSR0] ;low 8 bits of data from table
        BTFSC STATUS, Z ;end of text = 0
        RETURN
        CALL TX_Serial
        INCF FSR0L
        BTFSC STATUS, Z ;table page crossover?
        INCF FSR0H ;yes
        GOTO Send_Char

;-----------------------------------
; Serial port routines
;-----------------------------------

Init_Serial NOP
        BANKSEL TXSTA ;bank3
        BSF TXSTA, BRGH ;high speed mode
        MOVLW d'51' ;9600 baud at 8-MHz
        MOVWF SPBRG
        BANKSEL PIR1 ;bank0
        BCF PIR1, RCIF ;clear RX interrupt
        BANKSEL RCSTA ;bank3
        BSF RCSTA, SPEN ;serial port enable
        BSF RCSTA, CREN ;continuous RX enable
        BCF TXSTA, SYNC ;asynchronous mode
        BSF TXSTA, TXEN ;enable transmitter
        BANKSEL PORTA ;bank0
        RETURN

RX_Serial NOP
        BANKSEL RCSTA ;bank3
        BTFSC RCSTA, OERR
        CALL Overflow
        BANKSEL PIR1 ;bank0
        BTFSS PIR1, RCIF ;RX interrupt
        GOTO RX_Serial
        BANKSEL RCREG
        MOVFW RCREG ;read RX buffer (clears interrupt)
        BANKSEL PORTA ;bank0
        RETURN

TX_Serial NOP
        BANKSEL PIR1 ;bank0
        BTFSS PIR1, TXIF ;TX interrupt: 1 = TXREG is empty
        GOTO TX_Serial ;not empty
        BANKSEL TXREG ;bank3
        MOVWF TXREG ;ok to transmit
        BANKSEL PORTA ;bank0
        RETURN

Overflow BCF RCSTA, CREN ;clear overflow by disabling receiver
        BSF RCSTA, CREN ;re-enable receiver
        RETURN

;--------------------------------------------------------------------------
; Write serial data to RF Transmitter module
;--------------------------------------------------------------------------

Output_RF MOVLW d'3' ;send command three times
        MOVWF Dummy
Out_RF1 MOVFW RF_Byte1
        CALL Write_RF
        MOVFW RF_Byte2
        CALL Write_RF
        MOVFW RF_Byte3
        CALL Write_RF
        CALL Stop_Bit
        CALL DelaySync
        DECFSZ Dummy, F
        GOTO Out_RF1
        RETURN

Write_RF MOVWF Data_Byte ;Send what's in W
    MOVLW 0x08 ;8 bits to send
    MOVWF BitCount
Wrtloop BSF Serial_RF
        RLF Data_Byte, F ;MSB sent first
        BTFSC STATUS, C ;Test the carry bit
        GOTO OneBit
ZeroBit CALL DelayShort
        BCF Serial_RF
        CALL DelayLong
        GOTO Check_Cnt
OneBit CALL DelayLong
        BCF Serial_RF
        CALL DelayShort
Check_Cnt DECFSZ BitCount, F
        GOTO Wrtloop
        RETURN

Stop_Bit BSF Serial_RF
        CALL DelayShort
        BCF Serial_RF
        RETURN

;-----------------------------------
; Delay routines (8-MHz clock)
;-----------------------------------

DelayShort CALL Delay100us
        MOVLW d'43'
        GOTO Cntdwn

DelayLong CALL Delay500us
        MOVLW d'31'
        GOTO Cntdwn

DelaySync CALL Delay5ms
        CALL Delay500us
        CALL Delay100us
        MOVLW d'12'
        GOTO Cntdwn

Delay100us MOVLW d'49'
        GOTO Cntdwn

Delay500us MOVLW d'249'
        GOTO Cntdwn

Delay1ms MOVLW d'249'
        CALL Cntdwn
        MOVLW d'249'
        GOTO Cntdwn

Delay5ms MOVLW d'5'
        MOVWF DelayCount
loop5ms CALL Delay1ms
        DECFSZ DelayCount, F
        GOTO loop5ms
        RETURN

Delay10ms MOVLW d'10'
        MOVWF DelayCount
loop10ms CALL Delay1ms
        DECFSZ DelayCount, F
        GOTO loop10ms
        RETURN

Delay100ms MOVLW d'100'
        MOVWF DelayCount
loop100ms CALL Delay1ms
        DECFSZ DelayCount, F
        GOTO loop100ms
        RETURN

Delay1sec CALL Delay100ms
        CALL Delay100ms
        CALL Delay100ms
        CALL Delay100ms
        CALL Delay100ms
        CALL Delay100ms
        CALL Delay100ms
        CALL Delay100ms
        CALL Delay100ms
        GOTO Delay100ms

Cntdwn ADDLW -1 ;decrement W
        BTFSS STATUS, Z ;Zero flag set?
        GOTO Cntdwn ;No, keep looping
        RETURN ;Yes, timeout done

;-----------------------------------
; Strings
;-----------------------------------

Strings CODE 0x1000

Command1
 dt "AT+CIPMUX=1",0x0D,0x0A,0x00

Command2
 dt "AT+CIPSERVER=1,40100",0x0D,0x0A,0x00

Command3
 dt "AT+CIPSEND=0,",0x00 ;(code fills in rest of command)

Command4
 dt "AT+CIPCLOSE=0",0x0D,0x0A,0x00

Msg_Begin
 dt "<circle cx=25 cy=",0x00

Msg_Green
 dt "r=20 stroke=black stroke-width=4 fill=green />",0x00

Msg_Red
 dt "r=20 stroke=black stroke-width=4 fill=red />",0x00

Msg_White
 dt "r=20 stroke=black stroke-width=4 fill=white />",0x00

Message1
 dt "50 ",0x00

Message2
 dt "100 ",0x00

Message3
 dt "150 ",0x00

Message4
 dt "200 ",0x00

Message5
 dt "250 ",0x00

Bad_Msg
 dt "Bad Command",0x00

HTML_Open
 dt "<html><svg height=350 width=100>",0x00 ;(HTML open and SVG open)

HTML_Close
 dt "</svg></html>",0x00 ;(SVG close and HTML close)

;-------------------------------------------------------------------------------

        END