; ****************************************************************
; Electronic Wallet using the PN522 RFID Module
; Uses 13.56-MHz MIFARE Classic 1k tags/cards
;
; Assumes that we are using the default 8-MHz internal clock.
;
; All routines will exit pointing to bank0.
; ****************************************************************
;
        LIST P=PIC16F688
        #INCLUDE <p16f688.inc>

        ERRORLEVEL	0,	-302	;suppress bank selection messages

        __CONFIG _FOSC_INTOSCIO & _WDT_OFF & _PWRTE_ON & _MCLRE_OFF & _BOD_OFF & _CPD_OFF & _CP_OFF

; Control lines for the LCD interface
LCD_Data4 EQU 0 ;RC0: LCD data line 4
LCD_Data5 EQU 1 ;RC1: LCD data line 5
LCD_Data6 EQU 2 ;RC2: LCD data line 6
LCD_Data7 EQU 3 ;RC3: LCD data line 7
#define LCD_TRIS TRISC
#define LCD_PORT PORTC
#define Max_Line 8 ;Max hex chars per line (1 hex = 2 ASCII)

; PORTA Defines
#define Enable_T TRISA, 0 ;LCD enable
#define Enable PORTA, 0 ;LCD enable
#define Select_T TRISA, 1 ;LCD cmd/data mode select
#define Select PORTA, 1 ;LCD cmd/data mode select
#define Init_Sw PORTA, 2 ;0=zero the credits and change the keys
#define Inc_Sw PORTA, 3 ;0=increment, 1=decrement

Cmnd_Mode EQU 00 ;LCD register select command mode
Data_Mode EQU 01 ;LCD register select data mode

#define Firm_Vers 0x92 ;Module firware version (0x91 or 0x92)

#define Trail_Blk d'7' ;ID of Trailer Block (holds keys)
#define Data_Blk d'6' ;ID of Data Block (holds credits)
#define Bkup_Blk d'5' ;ID of Backup Data Block (holds credits)

#define Def_Key1 0xFF ;first byte of default key
#define Def_Key2 0xFF
#define Def_Key3 0xFF
#define Def_Key4 0xFF
#define Def_Key5 0xFF
#define Def_Key6 0xFF ;last byte of default key

#define My_Key1 0x01 ;first byte of new key
#define My_Key2 0x02
#define My_Key3 0x00
#define My_Key4 0x01
#define My_Key5 0x04
#define My_Key6 0x08 ;last byte of new key

;Set for increment amount (packed BCD)
#define Inc1 0x00 ;1/10
#define Inc100 0x00 ;100/1000
#define Inc10_000 0x00 ;10/100 thousand
#define Inc_Mill 0x02 ;1/10 million

;Set for decrement amount (packed BCD)
#define Dec1 0x00 ;1/10
#define Dec100 0x00 ;100/1000
#define Dec10_000 0x50 ;10/100 thousand
#define Dec_Mill 0x00 ;1/10 million

;Defines
RX_Port EQU 05 ;PORTC5 - Serial receive
TX_Port EQU 04 ;PORTC4 - Serial transmit (unused)

Bank0_Data UDATA 0x20 ;Bank 0 data
Delay_Cnt RES 1 ;Counter
LCD_Data RES 1 ;Temporary holder for LCD data
Reg_Select RES 1 ;LCD register select flag
BCD_Byte RES 1 ;used for conversion to ASCII
Temp_ASC RES 1 ;Temporary variable used in Make_ASCII
Byte_Count RES 1 ;byte counter
RX_Byte RES 1 ;serial receive byte
Dummy RES 1 ;temporary variable
New_Msg RES 1 ;new message received flag
Save_W RES 1 ;save the W register during interrupts
Save_Status RES 1 ;save the Status register during interrupts
UID1 RES 1 ;user ID of card/tag
UID2 RES 1 ;user ID of card/tag
UID3 RES 1 ;user ID of card/tag
UID4 RES 1 ;user ID of card/tag
UID_BCC RES 1 ;Block Check Character (XOR of UID)
Try_Def RES 1 ;if scan fails then try default key
FIFO_Data RES 1 ;temporary holder for FIFO byte
Line_Brk RES 1 ;LCD line break after this value
CRC_L RES 1 ;buffer for CRC low value
CRC_H RES 1 ;buffer for CRC high value
Exp_Resp RES 1 ;expected response to module commands
ATQA_L RES 1 ;Tag Answer-To-Request-A (low)
ATQA_H RES 1 ;Tag Answer-To-Request-A (high)
Carry RES 1 ;carry flag from DAA routine
Borrow RES 1 ;borrow flag from DAS routine
Millions RES 1 ;Packed BCD (millions and 10 millions)
Ten_Thou RES 1 ;Packed BCD (10 thousands and 100 thousands)
Hundreds RES 1 ;Packed BCD (hundreds and thousands)
Ones RES 1 ;Packed BCD (ones and tens)
Tag_Blk_Num RES 1 ;Tag Block Number
Comp_1 RES 1 ;1's complement credit amount LS byte
Comp_2 RES 1
Comp_3 RES 1
Comp_4 RES 1 ;1's complement credit amount MS byte
Reinit_Tag RES 1 ;tag data corrupt so try reinit

Tag_Message UDATA 0x50 ;ACK, Preamble, Message Response
Byte1 RES 1 ;First byte
Byte2 RES 1
Byte3 RES 1
Byte4 RES 1
Byte5 RES 1
Byte6 RES 1
Byte7 RES 1
Byte8 RES 1
More_Bytes RES d'15' ;only needed during debug to dump data

;-----------------------------------
; Macros
;-----------------------------------

;Decimal adjust passed argument after BCD addition
DAA macro var1
        MOVFW var1
        ADDLW -0x0A
        BTFSC STATUS, DC ;LSD > 9?
        ADDLW 0x06 ;yes so fix it
        ADDLW 0x0A ;add back in what we took out
        CLRF Carry
        ADDLW -0xA0
        BTFSC STATUS, C ;MSD > 9?
        BSF Carry, 0 ;yes
        ADDLW 0xA0 ;add back in what we took out
        BTFSC Carry, 0
        ADDLW 0x60
        MOVWF var1 ;copy result to passed in variable
        endm

;Decimal adjust passed argument after BCD subtraction
DAS macro var1
        MOVFW var1
        ADDLW 0x06
        BTFSC STATUS, DC ;LSD > 9?
        ADDLW -0x06 ;yes so fix it
        ADDLW -0x06 ;subtract back out what we put in
        CLRF Borrow
        ADDLW 0x60
        BTFSC STATUS, C ;MSD > 9?
        BSF Borrow, 0 ;yes
        ADDLW -0x60 ;subtract back out what we put in
        BTFSC Borrow, 0
        ADDLW -0x60
        MOVWF var1 ;copy result to passed in variable
        endm

;-----------------------------------
; Program code starts here
;-----------------------------------

RESET CODE 0x00
        GOTO Init

Int_Vec CODE 0x04
        BCF PIE1, RCIE ;serial RX interrupt enable
        MOVWF Save_W
        SWAPF STATUS, W
        MOVWF Save_Status
Chk_Ovr BTFSS RCSTA, OERR ;receive buffer overflow error:
        GOTO RX_Int1 ;no
        CALL Overflow
        GOTO Ret_Prep

RX_Int1 MOVFW RCREG ;read RX buffer (clears interrupt)
        MOVWF RX_Byte
        BTFSC New_Msg, 0 ;first character of new message?
        GOTO RX_Int2 ;no
        CLRF Byte_Count

RX_Int2 BSF New_Msg, 0
        MOVLW LOW Byte1
        ADDWF Byte_Count, W
        MOVWF FSR
        MOVFW RX_Byte
        MOVWF INDF ;save to buffer as indexed by Byte_Count
        INCF Byte_Count, F

RX_Int3 MOVFW RX_Byte
        BTFSC PIR1, RCIF ;another RX interrupt?
        GOTO Chk_Ovr ;yes

Ret_Prep SWAPF Save_Status, W
        MOVWF STATUS
        SWAPF Save_W, F
        SWAPF Save_W, W
        BSF PIE1, RCIE ;serial RX interrupt enable
        RETFIE

Init NOP ;error if go directly to BANKSEL
        BANKSEL TRISA ;bank1
        BCF Enable_T ;output
        BCF Select_T ;output
        BCF LCD_TRIS, LCD_Data4
        BCF LCD_TRIS, LCD_Data5
        BCF LCD_TRIS, LCD_Data6
        BCF LCD_TRIS, LCD_Data7
        CLRF ANSEL ;set all as digital
        MOVLW 0x70
        MOVWF OSCCON ;set for 8-MHz internal clock
        BCF OPTION_REG, NOT_RAPU ;enable weak pull-ups
        BSF PIE1, RCIE ;serial RX interrupt enable

        BANKSEL PORTA ;bank0
        MOVLW 0x07
        MOVWF CMCON0 ;turn off comparators
        CLRF Byte_Count
        CLRF New_Msg
        CALL Init_Serial

        BTFSS STATUS, NOT_TO ;reset due to WDT?
        GOTO Scan_Loop ;yes
        CLRF Try_Def
        CALL Delay100ms ;wait for LCD to get ready
        CALL Init_LCD

Module_Init CALL Startup
wait_start BTFSS New_Msg, 0
        GOTO wait_start
        MOVLW Firm_Vers ;firmware version (91 or 92)
        SUBWF Byte1, W
        BTFSC STATUS, Z ;received version number?
        GOTO Scan_Loop ;yes
        CLRF New_Msg
        GOTO Module_Init

Scan_Loop MOVLW Data_Blk
        MOVWF Tag_Blk_Num

        ;Need to clear the crypto flag before each scan
        CALL Clr_Crypto

        ;Find a tag
        CALL Scan_Tag
        CALL Disp_UID ;comment out if not needed

        ;Found a tag, now select it
        CALL Select_Tag
        CALL Select_Msg ;comment out if not needed

        ;Authenticate for reads/writes
        CALL Auth_Tag
        CALL Auth_Msg ;comment out if not needed

        ;Manual init switch
        BTFSS Init_Sw ;initialize tag?
        CALL Init_Tag ;yes

        ;Initialize a new tag (change keys and set credits to zero)
        ;This is done if the tag cannot be authorized using My_Key
        BTFSC Try_Def, 0
        CALL Init_Tag

        ;Attempt to initialize a tag if both sets of data are corrupted
        BTFSC Reinit_Tag, 0
        CALL Init_Tag

        ;Read data
        CALL Read_Tag
        CALL Get_Credit
        SUBLW d'1'
        BTFSS STATUS, Z ;valid data?
        GOTO Match_Fail ;no
        CALL Disp_Credit

        BTFSS Inc_Sw ;add credits?
        CALL Inc_Credit ;yes
        BTFSC Inc_Sw ;subtract credits?
        CALL Dec_Credit ;yes

        CALL Done_Msg

        GOTO Scan_Loop

;-----------------------------------
; 522 Module Commands
;-----------------------------------
Startup CALL Dummy_Data ;returns either 0x00 or nothing
        CALL Soft_Reset
        ;CALL RX_Gain48
        CALL ASK100_Cmd
        CALL CRC_6363
        CALL Antenna_On
        CALL FW_Version
        RETURN

;Board may power up thinking a command without data has been received.
;Neither a SW nor a HW reset corrects this so send a dummy byte. If
;the byte is interpreted as a command it will be harmless.
Dummy_Data MOVLW 0x80 ;read reserved register 00
        CALL TX_Serial
        CALL Delay2ms
        RETURN

;Reset the module
Soft_Reset MOVLW 0x01 ;write CommandReg
        CALL TX_Serial
        MOVLW 0x0F ;reset 522
        CALL TX_Serial
        CALL Delay10ms
        RETURN

;Set receiver gain to the maximum
RX_Gain48 CLRF New_Msg
        MOVLW 0x26 ;write RFCfgReg
        MOVWF Exp_Resp
        CALL TX_Serial
        MOVLW 0x70 ;RX Gain = 48 dB
        CALL TX_Serial
        CALL Delay2ms
        CALL Chk_Resp
        RETURN

;Set Amplitude Shift Key modulation to 100%
ASK100_Cmd CLRF New_Msg
        MOVLW 0x15 ;write TxASKReg
        MOVWF Exp_Resp
        CALL TX_Serial
        MOVLW 0x40 ;100% ASK
        CALL TX_Serial
        CALL Delay2ms
        CALL Chk_Resp
        RETURN

;Set CRC calculation preset value to 6363h
CRC_6363 CLRF New_Msg
        MOVLW 0x11 ;write ModeReg
        MOVWF Exp_Resp
        CALL TX_Serial
        MOVLW 0x3D ;CRC preset = 6363h
        CALL TX_Serial
        CALL Delay2ms
        CALL Chk_Resp
        RETURN

;Turn antenna on (0x03). Hardcoded to included the default
;value of 0x80 (TX2 signal inverted when TX2 enabled).
Antenna_On CLRF New_Msg
        MOVLW 0x14 ;write TxControlReg
        MOVWF Exp_Resp
        CALL TX_Serial
        MOVLW 0x83 ;Antenna On, RX2 inverted
        CALL TX_Serial
        CALL Delay2ms
        CALL Chk_Resp
        RETURN

;Read module firmware version (0x91 or 0x92)
FW_Version CLRF New_Msg
        MOVLW 0xB7 ;read VersionReg
        CALL TX_Serial
        CALL Delay2ms
        MOVLW Firm_Vers
        MOVWF Exp_Resp
        CALL Chk_Resp
        RETURN

;Read the command register (results vary)
Read_Cmd MOVLW 0x81 ;read CommandReg
        CALL TX_Serial
        CALL Delay2ms
        RETURN

;Clear current command
Idle_Cmd CLRF New_Msg
        MOVLW 0x01 ;write CommandReg
        MOVWF Exp_Resp
        CALL TX_Serial
        MOVLW 0x00 ;set to idle
        CALL TX_Serial
        CALL Delay2ms
        CALL Chk_Resp
        RETURN

;Mifare defines REQA and WUPA as 7-bit commands
Bits7_Cmd CLRF New_Msg
        MOVLW 0x0D ;write BitFramingReg
        MOVWF Exp_Resp
        CALL TX_Serial
        MOVLW 0x07 ;use 7 bits of last byte in FIFO
        CALL TX_Serial
        CALL Delay2ms
        CALL Chk_Resp
        RETURN

;All Mifare commands except REQA and WUPA are 8-bits
Bits8_Cmd CLRF New_Msg
        MOVLW 0x0D ;write BitFramingReg
        MOVWF Exp_Resp
        CALL TX_Serial
        MOVLW 0x00 ;use all 8 bits of FIFO bytes
        CALL TX_Serial
        CALL Delay2ms
        CALL Chk_Resp
        RETURN

;Number of bytes in the response from the tag
FIFO_Level MOVLW 0x8A ;read FIFOLevelReg
        CALL TX_Serial
        CALL Delay2ms
        RETURN

;Zero out FIFO byte count
Flush_FIFO CLRF New_Msg
        MOVLW 0x0A ;write FIFOLevelReg
        MOVWF Exp_Resp
        CALL TX_Serial
        MOVLW 0x80 ;resets FIFO buffer pointer
        CALL TX_Serial
        CALL Delay2ms
        CALL Chk_Resp
        RETURN

;Commands and data sent to the tag must be written to the FIFO.
;Byte to be written is assumed to be in the W register.
Write_FIFO MOVWF FIFO_Data
        CLRF New_Msg
        MOVLW 0x09 ;write FIFODataReg
        MOVWF Exp_Resp
        CALL TX_Serial
        MOVFW FIFO_Data
        CALL TX_Serial
        CALL Delay2ms
        CALL Chk_Resp
        RETURN

;Transfer a byte from the FIFO to the serial port (PIC receives it)
Read_FIFO MOVLW 0x89 ;read FIFODataReg
        CALL TX_Serial
        CALL Delay2ms
        RETURN

;Transmit bytes in the FIFO to the tag then turn on the receiver
Transceive MOVLW 0x01 ;write CommandReg
        CALL TX_Serial
        MOVLW 0x0C ;transmit FIFO data then activate receiver
        CALL TX_Serial
        CALL Delay2ms
        CLRF New_Msg
        MOVLW 0x8D ;read BitFramingReg
        CALL TX_Serial
transcv_1 CALL Delay1ms
        BTFSS New_Msg, 0 ;response received?
        GOTO transcv_1 ;no
        MOVLW 0x0D ;write BitFramingReg
        CALL TX_Serial
        MOVFW Byte1 ;current value
        IORLW 0x80 ;start transmission
        CALL TX_Serial
        CALL Delay10ms
        RETURN

;Authenticate the tag
Auth_Cmd CLRF New_Msg
        MOVLW 0x01 ;write CommandReg
        MOVWF Exp_Resp
        CALL TX_Serial
        MOVLW 0x0E ;authenticate tag
        CALL TX_Serial
        CALL Delay10ms
        CALL Chk_Resp
        RETURN

;Calculate the CRC for the bytes in the FIFO
;NOTE: This resets the FIFO_Level to zero
Calc_CRC CLRF New_Msg
        MOVLW 0x01 ;write CommandReg
        MOVWF Exp_Resp
        CALL TX_Serial
        MOVLW 0x03 ;calculate CRC for FIFO data
        CALL TX_Serial
        CALL Delay2ms
        CALL Chk_Resp
        RETURN

;Read the high byte of the CRC
Read_CRC_H MOVLW 0xA1 ;read CRCResultReg (high)
        CALL TX_Serial
        CALL Delay2ms
        RETURN

;Read the low byte of the CRC
Read_CRC_L MOVLW 0xA2 ;read CRCResultReg (low)
        CALL TX_Serial
        CALL Delay2ms
        RETURN

;Read Staus Register 1
Read_Stat1 MOVLW 0x87 ;read Status1Reg
        CALL TX_Serial
        CALL Delay2ms
        RETURN

;Read Status Register 2
Read_Stat2 MOVLW 0x88 ;read Status2Reg
        CALL TX_Serial
        CALL Delay2ms
        RETURN

;Read the Error Flag register
Read_Error MOVLW 0x86 ;read ErrorReg
        CALL TX_Serial
        CALL Delay2ms
        RETURN

;Clears Status Register 2 which includes the Crypto_On flag
;Crypto_On gets set when a tag is authenticated and must be
;cleared before another scan is attempted.
Clr_Crypto CLRF New_Msg
        MOVLW 0x08 ;write Status2Reg
        MOVWF Exp_Resp
        CALL TX_Serial
        MOVLW 0x00 ;clear crypto on flag
        CALL TX_Serial
        CALL Delay2ms
        CALL Chk_Resp
        RETURN

;Utility to check for a valid command response.
;Writes to a register will return an echo of the register number.
;Reads of a register may return multiple bytes.
Chk_Resp BTFSS New_Msg, 0 ;response received?
        GOTO No_Resp ;no
        MOVFW Byte1 ;should be response
        SUBWF Exp_Resp, W
        BTFSS STATUS, Z ;match?
        GOTO Bad_Resp ;no
        RETURN

;-----------------------------------
; RFID Card/Tag Commands
;-----------------------------------
;Sending commands to the card/tag requires putting the information into the
;MFRC522 module FIFO. First the command, second the data (if any), last the
;checksum. The MFRC522 module can be commanded to calculate the checksums
;which is then read out so it can be written to the FIFO. Lastly, a Transceive
;or Authenticate command is sent.

;Look for a tag
Scan_Tag CALL Scan_Msg
        CALL Idle_Cmd
        CALL Flush_FIFO
        MOVLW 0x26 ;REQA
        CALL Write_FIFO
        CALL Bits7_Cmd
        CALL Transceive
        CLRF New_Msg
        CALL FIFO_Level
        MOVFW Byte1
        BTFSC STATUS, Z ;received tag type?
        GOTO Scan_Tag ;no
        MOVLW 0x02 ;Tag type is two digits
        MOVWF Exp_Resp
        CALL Chk_Resp
        CALL Read_FIFO
        CALL Read_FIFO
        MOVFW Byte2
        MOVWF ATQA_L
        MOVFW Byte3
        MOVWF ATQA_H
        ;Add check for tag type here if desired.
        ;Mifare Classic (1k) = 0004h
        CALL Get_UID
        RETURN

Get_UID CALL Idle_Cmd
        CALL Flush_FIFO
        MOVLW 0x93 ;CL1
        CALL Write_FIFO
        MOVLW 0x20 ;Anticollision
        CALL Write_FIFO
        CALL Bits8_Cmd
        CALL Transceive
        CLRF New_Msg
        CALL Read_FIFO
        CALL Read_FIFO
        CALL Read_FIFO
        CALL Read_FIFO
        MOVFW Byte1
        MOVWF UID1
        MOVFW Byte2
        MOVWF UID2
        MOVFW Byte3
        MOVWF UID3
        MOVFW Byte4
        MOVWF UID4
        RETURN

Select_Tag CALL Idle_Cmd
        CALL Flush_FIFO
        MOVLW 0x93 ;CL1
        CALL Write_FIFO
        MOVLW 0x70 ;Select
        CALL Write_FIFO
        MOVFW UID1
        MOVWF UID_BCC
        CALL Write_FIFO
        MOVFW UID2
        XORWF UID_BCC, F
        CALL Write_FIFO
        MOVFW UID3
        XORWF UID_BCC, F
        CALL Write_FIFO
        MOVFW UID4
        XORWF UID_BCC, F
        CALL Write_FIFO
        MOVFW UID_BCC
        CALL Write_FIFO
        CALL Calc_CRC
        CLRF New_Msg
        CALL Read_CRC_H
        CALL Read_CRC_L
        MOVFW Byte1
        MOVWF CRC_H
        MOVFW Byte2
        MOVWF CRC_L
        ;Calc_CRC flushes the FIFO buffer so need to reload
        CALL Idle_Cmd
        MOVLW 0x93 ;CL1
        CALL Write_FIFO
        MOVLW 0x70 ;Select
        CALL Write_FIFO
        MOVFW UID1
        CALL Write_FIFO
        MOVFW UID2
        CALL Write_FIFO
        MOVFW UID3
        CALL Write_FIFO
        MOVFW UID4
        CALL Write_FIFO
        MOVFW UID_BCC
        CALL Write_FIFO
        MOVFW CRC_L
        CALL Write_FIFO
        MOVFW CRC_H
        CALL Write_FIFO
        CALL Transceive
        CLRF New_Msg
        CALL FIFO_Level
        MOVLW 0x03 ;SAK + two byte checksum
        MOVWF Exp_Resp
        CALL Chk_Resp
        CLRF New_Msg
        CALL Read_FIFO
        MOVLW 0x08 ;SAK (Select Acknowledge)
        MOVWF Exp_Resp
        CALL Chk_Resp
        RETURN

;Authenticate tag data sector using the defined Trailer block ID
Auth_Tag CALL Idle_Cmd
        CALL Flush_FIFO
        MOVLW 0x60 ;authenticate with Key A
        CALL Write_FIFO
        MOVLW Trail_Blk ;Trailer block for data sector
        CALL Write_FIFO
        MOVLW My_Key1 ;Key A (6 bytes)
        BTFSC Try_Def, 0 ;failed previous scan?
        MOVLW Def_Key1 ;yes
        CALL Write_FIFO
        MOVLW My_Key2
        BTFSC Try_Def, 0 ;failed previous scan?
        MOVLW Def_Key2 ;yes
        CALL Write_FIFO
        MOVLW My_Key3
        BTFSC Try_Def, 0 ;failed previous scan?
        MOVLW Def_Key3 ;yes
        CALL Write_FIFO
        MOVLW My_Key4
        BTFSC Try_Def, 0 ;failed previous scan?
        MOVLW Def_Key4 ;yes
        CALL Write_FIFO
        MOVLW My_Key5
        BTFSC Try_Def, 0 ;failed previous scan?
        MOVLW Def_Key5 ;yes
        CALL Write_FIFO
        MOVLW My_Key6
        BTFSC Try_Def, 0 ;failed previous scan?
        MOVLW Def_Key6 ;yes
        CALL Write_FIFO ;end Key A
        MOVFW UID1 ;tag UID (4 bytes)
        CALL Write_FIFO
        MOVFW UID2
        CALL Write_FIFO
        MOVFW UID3
        CALL Write_FIFO
        MOVFW UID4
        CALL Write_FIFO ;end tag UID
        CALL Auth_Cmd
        CLRF New_Msg
        CALL Read_Stat2
        MOVLW 0x08 ;Crypto On flag
        ANDWF Byte1, W
        BTFSS STATUS, Z ;tag authenticated?
        RETURN ;yes
        GOTO Bad_Scan

;Requests contents of a data block. Data bytes (16) + two byte checksum
;will be returned in the FIFO.
Read_Tag CALL Idle_Cmd
        CALL Flush_FIFO
        MOVLW 0x30 ;Mifare read command
        CALL Write_FIFO
        MOVFW Tag_Blk_Num
        CALL Write_FIFO
        CALL Calc_CRC
        CLRF New_Msg
        CALL Read_CRC_H
        CALL Read_CRC_L
        MOVFW Byte1
        MOVWF CRC_H
        MOVFW Byte2
        MOVWF CRC_L
        ;Calc_CRC flushes the FIFO buffer so need to reload
        CALL Idle_Cmd
        MOVLW 0x30 ;Mifare read command
        CALL Write_FIFO
        MOVFW Tag_Blk_Num
        CALL Write_FIFO
        MOVFW CRC_L
        CALL Write_FIFO
        MOVFW CRC_H
        CALL Write_FIFO
        CALL Transceive
        CLRF New_Msg
        CALL FIFO_Level
        MOVLW 0x12 ;16 data bytes + 2 byte checksum
        SUBWF Byte1, W
        BTFSS STATUS, Z ;good read?
        GOTO Bad_Read ;no
        RETURN

;Initiates a write to the tag. Other routines are then called to
;store/modify data or change the keys.
Write_Tag CALL Idle_Cmd
        CALL Flush_FIFO
        MOVLW 0xA0 ;Read command
        CALL Write_FIFO
        MOVFW Tag_Blk_Num
        CALL Write_FIFO
        CALL Calc_CRC
        CLRF New_Msg
        CALL Read_CRC_H
        CALL Read_CRC_L
        MOVFW Byte1
        MOVWF CRC_H
        MOVFW Byte2
        MOVWF CRC_L
        ;Calc_CRC flushes the FIFO buffer so need to reload
        CALL Idle_Cmd
        MOVLW 0xA0 ;Read command
        CALL Write_FIFO
        MOVFW Tag_Blk_Num
        CALL Write_FIFO
        MOVFW CRC_L
        CALL Write_FIFO
        MOVFW CRC_H
        CALL Write_FIFO
        CALL Transceive
        CLRF New_Msg
        CALL Read_FIFO
        MOVLW 0x0A ;acknowledge
        SUBWF Byte1, W
        BTFSS STATUS, Z ;good write?
        GOTO Bad_Write ;no
        RETURN

;Sends credit data as part of the Write_Tag command.
;Formatted as 4 bytes credit, 4 bytes 1's complement of credit,
;8 bytes of zeros. Called once for the data block and once for
;the backup block.
Send_Data CALL Idle_Cmd
        CALL Flush_FIFO
        MOVFW Millions
        CALL Write_FIFO
        MOVFW Ten_Thou
        CALL Write_FIFO
        MOVFW Hundreds
        CALL Write_FIFO
        MOVFW Ones
        CALL Write_FIFO
        COMF Millions, W
        CALL Write_FIFO
        COMF Ten_Thou, W
        CALL Write_FIFO
        COMF Hundreds, W
        CALL Write_FIFO
        COMF Ones, W
        CALL Write_FIFO
        MOVLW 0x00
        CALL Write_FIFO
        MOVLW 0x00
        CALL Write_FIFO
        MOVLW 0x00
        CALL Write_FIFO
        MOVLW 0x00
        CALL Write_FIFO
        MOVLW 0x00
        CALL Write_FIFO
        MOVLW 0x00
        CALL Write_FIFO
        MOVLW 0x00
        CALL Write_FIFO
        MOVLW 0x00
        CALL Write_FIFO
        CALL Calc_CRC
        CLRF New_Msg
        CALL Read_CRC_H
        CALL Read_CRC_L
        MOVFW Byte1
        MOVWF CRC_H
        MOVFW Byte2
        MOVWF CRC_L
        ;Calc_CRC flushes the FIFO buffer so need to reload
        CALL Idle_Cmd
        MOVFW Millions
        CALL Write_FIFO
        MOVFW Ten_Thou
        CALL Write_FIFO
        MOVFW Hundreds
        CALL Write_FIFO
        MOVFW Ones
        CALL Write_FIFO
        COMF Millions, W
        CALL Write_FIFO
        COMF Ten_Thou, W
        CALL Write_FIFO
        COMF Hundreds, W
        CALL Write_FIFO
        COMF Ones, W
        CALL Write_FIFO
        MOVLW 0x00
        CALL Write_FIFO
        MOVLW 0x00
        CALL Write_FIFO
        MOVLW 0x00
        CALL Write_FIFO
        MOVLW 0x00
        CALL Write_FIFO
        MOVLW 0x00
        CALL Write_FIFO
        MOVLW 0x00
        CALL Write_FIFO
        MOVLW 0x00
        CALL Write_FIFO
        MOVLW 0x00
        CALL Write_FIFO
        MOVFW CRC_L
        CALL Write_FIFO
        MOVFW CRC_H
        CALL Write_FIFO
        CALL Transceive
        CLRF New_Msg
        CALL Read_FIFO
        MOVLW 0x0A ;acknowledge
        SUBWF Byte1, W
        BTFSS STATUS, Z ;good write?
        GOTO Bad_Write ;no
        RETURN

;Sends key data as part of the Write_Tag command.
;Formated as 6 bytes Key A, 3 bytes write access flags,
;1 byte Don't Care, 6 bytes Key B.
Send_Keys CALL Idle_Cmd
        CALL Flush_FIFO
        MOVLW My_Key1 ;write Key A
        CALL Write_FIFO
        MOVLW My_Key2
        CALL Write_FIFO
        MOVLW My_Key3
        CALL Write_FIFO
        MOVLW My_Key4
        CALL Write_FIFO
        MOVLW My_Key5
        CALL Write_FIFO
        MOVLW My_Key6
        CALL Write_FIFO
        MOVLW 0xFF ;write access flags
        CALL Write_FIFO
        MOVLW 0x07
        CALL Write_FIFO
        MOVLW 0x80
        CALL Write_FIFO
        MOVLW 0x69 ;don't care byte
        CALL Write_FIFO
        MOVLW My_Key1 ;write Key B
        CALL Write_FIFO
        MOVLW My_Key2
        CALL Write_FIFO
        MOVLW My_Key3
        CALL Write_FIFO
        MOVLW My_Key4
        CALL Write_FIFO
        MOVLW My_Key5
        CALL Write_FIFO
        MOVLW My_Key6
        CALL Write_FIFO
        CALL Calc_CRC
        CLRF New_Msg
        CALL Read_CRC_H
        CALL Read_CRC_L
        MOVFW Byte1
        MOVWF CRC_H
        MOVFW Byte2
        MOVWF CRC_L
        ;Calc_CRC flushes the FIFO buffer so need to reload
        CALL Idle_Cmd
        MOVLW My_Key1 ;write Key A
        CALL Write_FIFO
        MOVLW My_Key2
        CALL Write_FIFO
        MOVLW My_Key3
        CALL Write_FIFO
        MOVLW My_Key4
        CALL Write_FIFO
        MOVLW My_Key5
        CALL Write_FIFO
        MOVLW My_Key6
        CALL Write_FIFO
        MOVLW 0xFF ;write access flags
        CALL Write_FIFO
        MOVLW 0x07
        CALL Write_FIFO
        MOVLW 0x80
        CALL Write_FIFO
        MOVLW 0x69 ;Don't care byte
        CALL Write_FIFO
        MOVLW My_Key1 ;write Key B
        CALL Write_FIFO
        MOVLW My_Key2
        CALL Write_FIFO
        MOVLW My_Key3
        CALL Write_FIFO
        MOVLW My_Key4
        CALL Write_FIFO
        MOVLW My_Key5
        CALL Write_FIFO
        MOVLW My_Key6
        CALL Write_FIFO
        MOVFW CRC_L
        CALL Write_FIFO
        MOVFW CRC_H
        CALL Write_FIFO
        CALL Transceive
        CLRF New_Msg
        CALL Read_FIFO
        MOVLW 0x0A ;acknowledge
        SUBWF Byte1, W
        BTFSS STATUS, Z ;good write?
        GOTO Bad_Write ;no
        RETURN

;Called to initialize a new tag or one with corrupted data
Init_Tag CALL Write_Tag
        CLRF Millions
        CLRF Ten_Thou
        CLRF Hundreds
        CLRF Ones
        CALL Send_Data
        MOVLW Trail_Blk
        MOVWF Tag_Blk_Num
        CALL Write_Tag
        CALL Send_Keys
        GOTO Tag_Done

;Gets the credit value from the tag and verifies it against the
;complemented copy. Returns '1' if valid or '0' if invalid.
Get_Credit CALL Read_Tag
        CLRF New_Msg
        CALL Read_FIFO
        CALL Read_FIFO
        CALL Read_FIFO
        CALL Read_FIFO
        CALL Read_FIFO
        CALL Read_FIFO
        CALL Read_FIFO
        CALL Read_FIFO
        MOVFW Byte1
        MOVWF Millions
        MOVFW Byte2
        MOVWF Ten_Thou
        MOVFW Byte3
        MOVWF Hundreds
        MOVFW Byte4
        MOVWF Ones
        ;Read 1's complement version
        COMF Byte5, W
        MOVWF Comp_4
        COMF Byte6, W
        MOVWF Comp_3
        COMF Byte7, W
        MOVWF Comp_2
        COMF Byte8, W
        MOVWF Comp_1
        ;verify values
        MOVFW Millions
        SUBWF Comp_4, W
        BTFSS STATUS, Z ;match?
        RETLW d'0' ;no
        MOVFW Ten_Thou
        SUBWF Comp_3, W
        BTFSS STATUS, Z ;match?
        RETLW d'0' ;no
        MOVFW Hundreds
        SUBWF Comp_2, W
        BTFSS STATUS, Z ;match?
        RETLW d'0' ;no
        MOVFW Ones
        SUBWF Comp_1, W
        BTFSS STATUS, Z ;match?
        RETLW d'0' ;no
        RETLW d'1' ;valid data

Get_Backup MOVLW Bkup_Blk ;Backup Block
        MOVWF Tag_Blk_Num
        CALL Read_Tag
        CALL Get_Credit
        SUBLW d'1'
        BTFSS STATUS, Z ;valid data?
        GOTO Bad_Card ;no
        RETURN

Match_Fail CALL Bad_Data
        CALL Delay1sec
        CALL Delay1sec
        CALL Get_Backup
        MOVLW Data_Blk ;Data Block
        MOVWF Tag_Blk_Num
        CALL Write_Tag
        CALL Send_Data
        CALL Read_Tag
        CALL Get_Credit
        SUBLW d'1'
        BTFSS STATUS, Z ;valid data?
        GOTO Bad_Card ;no
        CALL Data_Fixed
        CALL Delay1sec
        CALL Delay1sec
        CALL Disp_Credit
        CALL Delay1sec
        CALL Delay1sec
        CALL Done_Msg
        GOTO Scan_Loop

Inc_Credit MOVLW Inc1
        ADDWF Ones, F
        DAA Ones
        BTFSC Carry, 0
        INCF Hundreds, F
        MOVLW Inc100
        ADDWF Hundreds, F
        DAA Hundreds
        BTFSC Carry, 0
        INCF Ten_Thou, F
        MOVLW Inc10_000
        ADDWF Ten_Thou, F
        DAA Ten_Thou
        BTFSC Carry, 0
        INCF Millions, F
        MOVLW Inc_Mill
        ADDWF Millions, F
        DAA Millions
        BTFSC Carry, 0
        GOTO Full_Credit
        MOVLW Bkup_Blk ;Backup Block
        MOVWF Tag_Blk_Num
        CALL Write_Tag
        CALL Send_Data
        MOVLW Data_Blk ;Data Block
        MOVWF Tag_Blk_Num
        CALL Write_Tag
        CALL Send_Data
        CALL Read_Tag
        CALL Get_Credit
        SUBLW d'1'
        BTFSS STATUS, Z ;valid data?
        GOTO Match_Fail ;no
        CALL Disp_Credit
        RETURN

Dec_Credit MOVLW Dec1
        SUBWF Ones, F
        DAS Ones
        BTFSC Borrow, 0
        DECF Hundreds, F
        MOVLW Dec100
        SUBWF Hundreds, F
        DAS Hundreds
        BTFSC Borrow, 0
        DECF Ten_Thou, F
        MOVLW Dec10_000
        SUBWF Ten_Thou, F
        DAS Ten_Thou
        BTFSC Borrow, 0
        DECF Millions, F
        MOVLW Dec_Mill
        SUBWF Millions, F
        DAS Millions
        BTFSC Borrow, 0
        GOTO Bad_Credit
        MOVLW Bkup_Blk ;Backup Block
        MOVWF Tag_Blk_Num
        CALL Write_Tag
        CALL Send_Data
        MOVLW Data_Blk ;Data Block
        MOVWF Tag_Blk_Num
        CALL Write_Tag
        CALL Send_Data
        CALL Read_Tag
        CALL Get_Credit
        SUBLW d'1'
        BTFSS STATUS, Z ;valid data?
        GOTO Match_Fail ;no
        CALL Disp_Credit
        RETURN

;-----------------------------------
; Data conversion routines
;-----------------------------------

; Find the first non-zero digit for display
Find_First MOVF Millions, F
        BTFSC STATUS, Z
        GOTO Find1
        SWAPF Millions, W
        ANDLW 0x0F
        BTFSS STATUS, Z
        GOTO Disp_10M
        GOTO Disp_1M
Find1 MOVF Ten_Thou, F
        BTFSC STATUS, Z
        GOTO Find2
        SWAPF Ten_Thou, W
        ANDLW 0x0F
        BTFSS STATUS, Z
        GOTO Disp_100k
        GOTO Disp_10k
Find2 MOVF Hundreds, F
        BTFSC STATUS, Z
        GOTO Find3
        SWAPF Hundreds, W
        ANDLW 0x0F
        BTFSS STATUS, Z
        GOTO Disp_1k
        GOTO Disp_100
Find3 SWAPF Ones, W
        ANDLW 0x0F
        BTFSS STATUS, Z
        GOTO Disp_10
        GOTO Disp_1

; Convert values to ASCII for display
Disp_10M SWAPF Millions, W
        ANDLW 0x0F
        IORLW 0x30
        CALL Write_LCD
Disp_1M MOVF Millions, W
        ANDLW 0x0F
        IORLW 0x30
        CALL Write_LCD
        MOVLW ','
        CALL Write_LCD
Disp_100k SWAPF Ten_Thou, W
        ANDLW 0x0F
        IORLW 0x30
        CALL Write_LCD
Disp_10k MOVF Ten_Thou, W
        ANDLW 0x0F
        IORLW 0x30
        CALL Write_LCD
Disp_1k SWAPF Hundreds, W
        ANDLW 0x0F
        IORLW 0x30
        CALL Write_LCD
        MOVLW ','
        CALL Write_LCD
Disp_100 MOVF Hundreds, W
        ANDLW 0x0F
        IORLW 0x30
        CALL Write_LCD
Disp_10 SWAPF Ones, W
        ANDLW 0x0F
        IORLW 0x30
        CALL Write_LCD
Disp_1 MOVF Ones, W
        ANDLW 0x0F
        IORLW 0x30
        CALL Write_LCD
        RETURN

;-----------------------------------
; Receive Buffer Utilities (debug)
;-----------------------------------

;Display receive buffer
Disp_Buff CLRF New_Msg
        CLRF Dummy
        MOVLW Max_Line
        MOVWF Line_Brk
disp_loop MOVLW LOW Byte1
        ADDWF Dummy, W
        MOVWF FSR
        MOVFW INDF ;read from memory as indexed by Dummy
        CALL Make_ASCII
        INCF Dummy, F
        DECF Byte_Count, F
        BTFSC STATUS, Z
        RETURN
        MOVFW Line_Brk
        SUBWF Dummy, W
        BTFSS STATUS, Z ;LCD Line1 full?
        GOTO disp_loop ;no
        CALL Init_Line2
        GOTO disp_loop

;Convert Hex to ASCII for LCD
Make_ASCII MOVWF BCD_Byte
        SWAPF BCD_Byte, W
        ANDLW 0x0F
        IORLW 0x30
        MOVWF Temp_ASC
        SUBLW 0x39 ;check to see if A-F
        BTFSC STATUS, C
        GOTO Mk_ASCII_1
        MOVLW d'7'
        ADDWF Temp_ASC, F
Mk_ASCII_1 MOVFW Temp_ASC
        CALL Write_LCD
        MOVFW BCD_Byte
        ANDLW 0x0F
        IORLW 0x30
        MOVWF Temp_ASC
        SUBLW 0x39 ;check to see if A-F
        BTFSC STATUS, C
        GOTO Mk_ASCII_2
        MOVLW d'7'
        ADDWF Temp_ASC, F
Mk_ASCII_2 MOVFW Temp_ASC
        CALL Write_LCD
        RETURN

;-----------------------------------
; Serial Port Routines
;-----------------------------------

Init_Serial CLRF New_Msg
        CLRF Byte_Count
        BSF TXSTA, BRGH ;high speed mode
        BSF BAUDCTL, BRG16
        MOVLW d'207'
        MOVWF SPBRG ;9600 baud at 8-MHz clock
        MOVFW RCREG ;clear interrupt
        BSF TXSTA, TXEN ;enable transmitter
        BSF RCSTA, SPEN ;serial port enable
        BSF RCSTA, CREN ;continuous RX enable
        BSF INTCON, PEIE ;peripheral interrupt enable
        BSF INTCON, GIE ;general interrupt enable
        RETURN

TX_Serial BTFSS PIR1, TXIF ;TX interrupt: 1 = TXREG is empty
        GOTO TX_Serial ;not empty
        MOVWF TXREG ;ok to transmit
        RETURN

Overflow BCF RCSTA, SPEN ;disable serial port
        MOVFW RCREG ;clear interrupt
        BSF RCSTA, SPEN ;enable serial port (reset)
        RETURN

;----------------------------------------
; LCD Routines
;----------------------------------------

Init_LCD CALL Delay100ms ;allow LCD time to reset
        MOVLW Cmnd_Mode ;all init done in LCD command mode
        MOVWF Reg_Select
        MOVLW 0x03 ;LCD sees 30 hex
        CALL Cmd_8_Bit
        CALL Delay4ms ;Delay greater than 4.1ms
        CALL Delay100us
        MOVLW 0x03 ;LCD sees 30 hex
        CALL Cmd_8_Bit
        CALL Delay100us ;Delay greater than 100us
        MOVLW 0x03 ;LCD sees 30 hex
        CALL Cmd_8_Bit
        CALL Delay100us ;Delay greater than 100us
        MOVLW 0x02 ;Set 4-bit mode (LCD sees 20 hex)
        CALL Cmd_8_Bit
        CALL Delay100us ;Delay greater than 100us
        MOVLW 0x28 ;Set for 4-bit mode, 16 chars, 2 lines
        CALL Write_LCD
        CALL Delay100us ;Delay greater than 100us
        MOVLW 0x01 ;clear display
        CALL Write_LCD
        CALL Delay4ms ;Delay greater than 4ms
        MOVLW 0x06 ;Entry mode, increment DDRAM, no shift
        CALL Write_LCD
        CALL Delay100us ;Delay greater than 100us
        MOVLW 0x0C ;Display on, cursor off
        CALL Write_LCD
        CALL Delay100us ;Delay greater than 100us
        MOVLW Data_Mode
        MOVWF Reg_Select
        RETURN

Cmd_8_Bit MOVWF LCD_PORT ;byte to write will be in W
        BCF Select ;set for command mode
        BSF Enable ;write data to LCD
        NOP
        BCF Enable
        RETURN

Write_LCD MOVWF LCD_Data ;byte to write will be in W
        SWAPF LCD_Data, W ;send upper nibble
        ANDLW 0x0F ;clear upper 4 bits of W
        MOVWF LCD_PORT
        BSF Select ;preset for data mode
        BTFSS Reg_Select, 0 ;0 = command mode, 1 = data mode
        BCF Select ;set for command mode instead
        CALL Delay50us
        BSF Enable ;write data to LCD
        NOP
        BCF Enable
        MOVFW LCD_Data ;send lower nibble
        ANDLW 0x0F ;clear upper 4 bits of W
        MOVWF LCD_PORT
        BSF Select ;preset for data mode
        BTFSS Reg_Select, 0 ;0 = command mode, 1 = data mode
        BCF Select ;set for command mode instead
        BSF Enable ;write data to LCD
        NOP
        BCF Enable
        RETURN

Init_Line2 MOVLW Cmnd_Mode
        MOVWF Reg_Select
        MOVLW 0xC0 ;write at start of line 2 (address 0x40)
        CALL Write_LCD
        CALL Delay100us
        MOVLW Data_Mode
        MOVWF Reg_Select
        RETURN

Clear_LCD MOVLW Cmnd_Mode
        MOVWF Reg_Select
        MOVLW 0x01 ;clear display
        CALL Write_LCD
        CALL Delay4ms
        MOVLW Data_Mode
        MOVWF Reg_Select
        RETURN

Scan_Msg CALL Clear_LCD
        MOVLW ' '
        CALL Write_LCD
        MOVLW 'R'
        CALL Write_LCD
        MOVLW 'E'
        CALL Write_LCD
        MOVLW 'A'
        CALL Write_LCD
        MOVLW 'D'
        CALL Write_LCD
        MOVLW 'Y'
        CALL Write_LCD
        MOVLW ' '
        CALL Write_LCD
        MOVLW 'T'
        CALL Write_LCD
        MOVLW 'O'
        CALL Write_LCD
        MOVLW ' '
        CALL Write_LCD
        MOVLW 'S'
        CALL Write_LCD
        MOVLW 'C'
        CALL Write_LCD
        MOVLW 'A'
        CALL Write_LCD
        MOVLW 'N'
        CALL Write_LCD
        CALL Delay1sec
        RETURN

Disp_UID CALL Clear_LCD
        MOVLW 'U'
        CALL Write_LCD
        MOVLW 'I'
        CALL Write_LCD
        MOVLW 'D'
        CALL Write_LCD
        MOVLW ':'
        CALL Write_LCD
        MOVLW ' '
        CALL Write_LCD
        MOVFW UID1
        CALL Make_ASCII
        MOVFW UID2
        CALL Make_ASCII
        MOVFW UID3
        CALL Make_ASCII
        MOVFW UID4
        CALL Make_ASCII
        CALL Delay1sec
        CALL Delay1sec
        RETURN

Disp_Credit CALL Clear_LCD
        MOVLW 'C'
        CALL Write_LCD
        MOVLW 'R'
        CALL Write_LCD
        MOVLW 'E'
        CALL Write_LCD
        MOVLW 'D'
        CALL Write_LCD
        MOVLW 'I'
        CALL Write_LCD
        MOVLW 'T'
        CALL Write_LCD
        MOVLW 'S'
        CALL Write_LCD
        MOVLW ':'
        CALL Write_LCD
        CALL Init_Line2
        CALL Find_First
        CALL Delay1sec
        RETURN

Bad_Credit CALL Clear_LCD
        MOVLW 'N'
        CALL Write_LCD
        MOVLW 'O'
        CALL Write_LCD
        MOVLW 'T'
        CALL Write_LCD
        MOVLW ' '
        CALL Write_LCD
        MOVLW 'E'
        CALL Write_LCD
        MOVLW 'N'
        CALL Write_LCD
        MOVLW 'O'
        CALL Write_LCD
        MOVLW 'U'
        CALL Write_LCD
        MOVLW 'G'
        CALL Write_LCD
        MOVLW 'H'
        CALL Write_LCD
        CALL Init_Line2
        MOVLW 'C'
        CALL Write_LCD
        MOVLW 'R'
        CALL Write_LCD
        MOVLW 'E'
        CALL Write_LCD
        MOVLW 'D'
        CALL Write_LCD
        MOVLW 'I'
        CALL Write_LCD
        MOVLW 'T'
        CALL Write_LCD
        MOVLW 'S'
        CALL Write_LCD
        GOTO Tilt

Full_Credit CALL Clear_LCD
        MOVLW 'W'
        CALL Write_LCD
        MOVLW 'A'
        CALL Write_LCD
        MOVLW 'L'
        CALL Write_LCD
        MOVLW 'L'
        CALL Write_LCD
        MOVLW 'E'
        CALL Write_LCD
        MOVLW 'T'
        CALL Write_LCD
        MOVLW ' '
        CALL Write_LCD
        MOVLW 'F'
        CALL Write_LCD
        MOVLW 'U'
        CALL Write_LCD
        MOVLW 'L'
        CALL Write_LCD
        MOVLW 'L'
        CALL Write_LCD
        GOTO Tilt

No_Resp CALL Clear_LCD
        MOVLW 'N'
        CALL Write_LCD
        MOVLW 'O'
        CALL Write_LCD
        MOVLW ' '
        CALL Write_LCD
        MOVLW 'R'
        CALL Write_LCD
        MOVLW 'E'
        CALL Write_LCD
        MOVLW 'S'
        CALL Write_LCD
        MOVLW 'P'
        CALL Write_LCD
        MOVLW 'O'
        CALL Write_LCD
        MOVLW 'N'
        CALL Write_LCD
        MOVLW 'S'
        CALL Write_LCD
        MOVLW 'E'
        CALL Write_LCD
        GOTO Tilt

Bad_Resp CALL Clear_LCD
        MOVLW 'B'
        CALL Write_LCD
        MOVLW 'A'
        CALL Write_LCD
        MOVLW 'D'
        CALL Write_LCD
        MOVLW ' '
        CALL Write_LCD
        MOVLW 'R'
        CALL Write_LCD
        MOVLW 'E'
        CALL Write_LCD
        MOVLW 'S'
        CALL Write_LCD
        MOVLW 'P'
        CALL Write_LCD
        MOVLW 'O'
        CALL Write_LCD
        MOVLW 'N'
        CALL Write_LCD
        MOVLW 'S'
        CALL Write_LCD
        MOVLW 'E'
        CALL Write_LCD
        CALL Init_Line2
        MOVLW 'E'
        CALL Write_LCD
        MOVLW 'X'
        CALL Write_LCD
        MOVLW 'P'
        CALL Write_LCD
        MOVLW 'E'
        CALL Write_LCD
        MOVLW 'C'
        CALL Write_LCD
        MOVLW 'T'
        CALL Write_LCD
        MOVLW ':'
        CALL Write_LCD
        MOVFW Exp_Resp
        CALL Make_ASCII
        MOVLW ' '
        CALL Write_LCD
        MOVLW 'G'
        CALL Write_LCD
        MOVLW 'O'
        CALL Write_LCD
        MOVLW 'T'
        CALL Write_LCD
        MOVLW ':'
        CALL Write_LCD
        MOVFW Byte1
        CALL Make_ASCII
        CALL Delay1sec
        CALL Delay1sec
        GOTO Tilt

Select_Msg CALL Clear_LCD
        MOVLW 'T'
        CALL Write_LCD
        MOVLW 'A'
        CALL Write_LCD
        MOVLW 'G'
        CALL Write_LCD
        MOVLW ' '
        CALL Write_LCD
        MOVLW 'S'
        CALL Write_LCD
        MOVLW 'E'
        CALL Write_LCD
        MOVLW 'L'
        CALL Write_LCD
        MOVLW 'E'
        CALL Write_LCD
        MOVLW 'C'
        CALL Write_LCD
        MOVLW 'T'
        CALL Write_LCD
        MOVLW 'E'
        CALL Write_LCD
        MOVLW 'D'
        CALL Write_LCD
        CALL Delay1sec
        RETURN

Bad_Scan CALL Clear_LCD
        MOVLW 'B'
        CALL Write_LCD
        MOVLW 'A'
        CALL Write_LCD
        MOVLW 'D'
        CALL Write_LCD
        MOVLW ' '
        CALL Write_LCD
        MOVLW 'S'
        CALL Write_LCD
        MOVLW 'C'
        CALL Write_LCD
        MOVLW 'A'
        CALL Write_LCD
        MOVLW 'N'
        CALL Write_LCD
        COMF Try_Def, F ;toggle flag (try other key)
Tilt BSF WDTCON, SWDTEN ;force watchdog timeout
tilt1 GOTO tilt1

Bad_Write CALL Clear_LCD
        MOVLW 'B'
        CALL Write_LCD
        MOVLW 'A'
        CALL Write_LCD
        MOVLW 'D'
        CALL Write_LCD
        MOVLW ' '
        CALL Write_LCD
        MOVLW 'W'
        CALL Write_LCD
        MOVLW 'R'
        CALL Write_LCD
        MOVLW 'I'
        CALL Write_LCD
        MOVLW 'T'
        CALL Write_LCD
        MOVLW 'E'
        CALL Write_LCD
        GOTO Tilt

Bad_Read CALL Clear_LCD
        MOVLW 'B'
        CALL Write_LCD
        MOVLW 'A'
        CALL Write_LCD
        MOVLW 'D'
        CALL Write_LCD
        MOVLW ' '
        CALL Write_LCD
        MOVLW 'R'
        CALL Write_LCD
        MOVLW 'E'
        CALL Write_LCD
        MOVLW 'A'
        CALL Write_LCD
        MOVLW 'D'
        CALL Write_LCD
        GOTO Tilt

Auth_Msg CALL Clear_LCD
        MOVLW 'A'
        CALL Write_LCD
        MOVLW 'U'
        CALL Write_LCD
        MOVLW 'T'
        CALL Write_LCD
        MOVLW 'H'
        CALL Write_LCD
        MOVLW 'E'
        CALL Write_LCD
        MOVLW 'N'
        CALL Write_LCD
        MOVLW 'T'
        CALL Write_LCD
        MOVLW 'I'
        CALL Write_LCD
        MOVLW 'C'
        CALL Write_LCD
        MOVLW 'A'
        CALL Write_LCD
        MOVLW 'T'
        CALL Write_LCD
        MOVLW 'E'
        CALL Write_LCD
        MOVLW 'D'
        CALL Write_LCD
        CALL Delay1sec
        RETURN

Bad_Card CALL Clear_LCD
        MOVLW 'B'
        CALL Write_LCD
        MOVLW 'A'
        CALL Write_LCD
        MOVLW 'D'
        CALL Write_LCD
        MOVLW ' '
        CALL Write_LCD
        MOVLW 'C'
        CALL Write_LCD
        MOVLW 'A'
        CALL Write_LCD
        MOVLW 'R'
        CALL Write_LCD
        MOVLW 'D'
        CALL Write_LCD
        BSF Reinit_Tag, 0
        GOTO Tilt

Bad_Data CALL Clear_LCD
        MOVLW 'D'
        CALL Write_LCD
        MOVLW 'A'
        CALL Write_LCD
        MOVLW 'T'
        CALL Write_LCD
        MOVLW 'A'
        CALL Write_LCD
        MOVLW ' '
        CALL Write_LCD
        MOVLW 'C'
        CALL Write_LCD
        MOVLW 'O'
        CALL Write_LCD
        MOVLW 'R'
        CALL Write_LCD
        MOVLW 'R'
        CALL Write_LCD
        MOVLW 'U'
        CALL Write_LCD
        MOVLW 'P'
        CALL Write_LCD
        MOVLW 'T'
        CALL Write_LCD
        MOVLW ':'
        CALL Write_LCD
        CALL Init_Line2
        MOVLW 'C'
        CALL Write_LCD
        MOVLW 'H'
        CALL Write_LCD
        MOVLW 'E'
        CALL Write_LCD
        MOVLW 'C'
        CALL Write_LCD
        MOVLW 'K'
        CALL Write_LCD
        MOVLW 'I'
        CALL Write_LCD
        MOVLW 'N'
        CALL Write_LCD
        MOVLW 'G'
        CALL Write_LCD
        MOVLW ' '
        CALL Write_LCD
        MOVLW 'B'
        CALL Write_LCD
        MOVLW 'A'
        CALL Write_LCD
        MOVLW 'C'
        CALL Write_LCD
        MOVLW 'K'
        CALL Write_LCD
        MOVLW 'U'
        CALL Write_LCD
        MOVLW 'P'
        CALL Write_LCD
        CALL Delay1sec
        RETURN

Data_Fixed CALL Clear_LCD
        MOVLW 'D'
        CALL Write_LCD
        MOVLW 'A'
        CALL Write_LCD
        MOVLW 'T'
        CALL Write_LCD
        MOVLW 'A'
        CALL Write_LCD
        MOVLW ' '
        CALL Write_LCD
        MOVLW 'R'
        CALL Write_LCD
        MOVLW 'E'
        CALL Write_LCD
        MOVLW 'P'
        CALL Write_LCD
        MOVLW 'A'
        CALL Write_LCD
        MOVLW 'I'
        CALL Write_LCD
        MOVLW 'R'
        CALL Write_LCD
        MOVLW 'E'
        CALL Write_LCD
        MOVLW 'D'
        CALL Write_LCD
        CALL Delay1sec
        RETURN

Done_Msg CALL Clear_LCD
        MOVLW 'R'
        CALL Write_LCD
        MOVLW 'E'
        CALL Write_LCD
        MOVLW 'M'
        CALL Write_LCD
        MOVLW 'O'
        CALL Write_LCD
        MOVLW 'V'
        CALL Write_LCD
        MOVLW 'E'
        CALL Write_LCD
        MOVLW ' '
        CALL Write_LCD
        MOVLW 'T'
        CALL Write_LCD
        MOVLW 'A'
        CALL Write_LCD
        MOVLW 'G'
        CALL Write_LCD
        CALL Delay1sec
        CALL Delay1sec
        RETURN

Tag_Done CALL Clear_LCD
        MOVLW 'T'
        CALL Write_LCD
        MOVLW 'A'
        CALL Write_LCD
        MOVLW 'G'
        CALL Write_LCD
        MOVLW ' '
        CALL Write_LCD
        MOVLW 'I'
        CALL Write_LCD
        MOVLW 'N'
        CALL Write_LCD
        MOVLW 'T'
        CALL Write_LCD
        MOVLW 'I'
        CALL Write_LCD
        MOVLW 'A'
        CALL Write_LCD
        MOVLW 'L'
        CALL Write_LCD
        MOVLW 'I'
        CALL Write_LCD
        MOVLW 'Z'
        CALL Write_LCD
        MOVLW 'E'
        CALL Write_LCD
        MOVLW 'D'
        CALL Write_LCD
        GOTO Tilt

;-----------------------------------
; Delay routines (8-MHz clock)
;-----------------------------------

Delay50us MOVLW d'24'
        GOTO Cntdwn

Delay100us MOVLW d'49'
        GOTO Cntdwn

Delay1ms MOVLW d'249'
        CALL Cntdwn
        MOVLW d'249'
        GOTO Cntdwn

Delay2ms CALL Delay1ms
        GOTO Delay1ms

Delay4ms CALL Delay2ms
        GOTO Delay2ms

Delay10ms MOVLW d'10'
        MOVWF Delay_Cnt
loop10ms CALL Delay1ms
        DECFSZ Delay_Cnt, F
        GOTO loop10ms
        RETURN

Delay100ms MOVLW d'100'
        MOVWF Delay_Cnt
loop100ms CALL Delay1ms
        DECFSZ Delay_Cnt, F
        GOTO loop100ms
        RETURN

Delay250ms MOVLW d'250'
        MOVWF Delay_Cnt
loop250ms CALL Delay1ms
        DECFSZ Delay_Cnt, F
        GOTO loop250ms
        RETURN

Delay1sec CALL Delay250ms
        CALL Delay250ms
        CALL Delay250ms
        CALL Delay250ms
        RETURN

Cntdwn ADDLW -1 ;decrement W
        BTFSS STATUS, Z ;Zero flag set?
        GOTO Cntdwn ;No, keep looping
        RETURN ;Yes, timeout done
;-------------------------------------------------------------------------------

        END