; ****************************************************************
; Slot Machine
;
; Uses a 4-bit interface to a 1601 (single row) LCD
; Hard wired for write-only (delays used in place of reading the
; busy flag)
;
; Assumes that we are using the default 8-MHz internal clock.
;
; All routines will exit pointing to bank0.
; ****************************************************************
;
        LIST P=PIC16F688
        #INCLUDE <p16f688.inc>

        ERRORLEVEL	0,	-302	;suppress bank selection messages

        __CONFIG _FOSC_INTOSCIO & _WDT_OFF & _PWRTE_ON & _MCLRE_OFF & _BOD_OFF & _CPD_OFF & _CP_OFF

; Control lines for the LCD interface
LCD_Data4 EQU 0 ;RC0: LCD data line 4
LCD_Data5 EQU 1 ;RC1: LCD data line 5
LCD_Data6 EQU 2 ;RC2: LCD data line 6
LCD_Data7 EQU 3 ;RC3: LCD data line 7
Select EQU 4 ;RC4: cmd/data mode select
Enable EQU 5 ;RC5: LCD enable

; Control lines for other peripherals
Click EQU 0 ;RA0: Click output
LED1 EQU 1 ;RA1: LED1 output
LED2 EQU 2 ;RA2: LED2 output
Coin_Sw EQU 3 ;RA3: Coin switch input
Door EQU 4 ;RA4: Jackpot door output
Sound EQU 5 ;RA5: Sound module trigger

Cmnd_Mode EQU 00 ;LCD register select command mode
Data_Mode EQU 01 ;LCD register select data mode
Num_Clicks EQU 4 ;Number of clicks between digit updates

        UDATA 0x20
Delay_Cnt RES 1 ;Counter
LCD_Data RES 1 ;Temporary holder for LCD data
Reg_Select RES 1 ;LCD register select flag
Random RES 1 ;Counter used or random number generation
Test_Cnt RES 1 ;Temporary storage for random count
Digit1 RES 1 ;First digit to display
Digit2 RES 1 ;Second digit to display
Digit3 RES 1 ;Third digit to display
Temp_Dig RES 1 ;Temporary holder for digit value
Temp_Adr RES 1 ;Temporary holder for LCD address
Click_Cnt RES 1 ;Click counter

;-----------------------------------
; Program code starts here
;-----------------------------------

RESET CODE 0x00
        GOTO Init

Int_Vec CODE 0x04
        RETFIE

Init NOP ;error if go directly to BANKSEL
        BANKSEL TRISC ;bank1
        CLRF TRISC ;all outputs
        CLRF ANSEL ;all digital
        BCF TRISA, Click ;output
        BCF TRISA, LED1 ;output
        BCF TRISA, LED2 ;output
        BCF TRISA, Door ;output
        BCF TRISA, Sound ;output
        MOVLW 0x70
        MOVWF OSCCON ;set for 8-MHz internal clock

        BANKSEL PORTC ;bank0
        MOVLW 0x07
        MOVWF CMCON0 ;turn off comparators
        CLRF PORTA
        CLRF PORTC
        CALL Init_LCD
        CALL Delay1sec

Main_Loop INCF Random
        BTFSS PORTA, Coin_Sw
        CALL Spin
        GOTO Main_Loop

Spin MOVFW Random
        MOVWF Test_Cnt
        MOVLW d'0'
        SUBWF Test_Cnt, W
        BTFSC STATUS, Z
        GOTO Zeros
        MOVLW d'8'
        SUBWF Test_Cnt, W
        BTFSC STATUS, Z
        GOTO Zeros
        MOVLW d'16'
        SUBWF Test_Cnt, W
        BTFSC STATUS, Z
        GOTO Zeros
        MOVLW d'24'
        SUBWF Test_Cnt, W
        BTFSC STATUS, Z
        GOTO Zeros

        MOVLW d'32'
        SUBWF Test_Cnt, W
        BTFSC STATUS, Z
        GOTO Ones
        MOVLW d'40'
        SUBWF Test_Cnt, W
        BTFSC STATUS, Z
        GOTO Ones
        MOVLW d'48'
        SUBWF Test_Cnt, W
        BTFSC STATUS, Z
        GOTO Ones
        MOVLW d'56'
        SUBWF Test_Cnt, W
        BTFSC STATUS, Z
        GOTO Ones

        MOVLW d'64'
        SUBWF Test_Cnt, W
        BTFSC STATUS, Z
        GOTO Twos
        MOVLW d'72'
        SUBWF Test_Cnt, W
        BTFSC STATUS, Z
        GOTO Twos
        MOVLW d'80'
        SUBWF Test_Cnt, W
        BTFSC STATUS, Z
        GOTO Twos
        MOVLW d'88'
        SUBWF Test_Cnt, W
        BTFSC STATUS, Z
        GOTO Twos

        MOVLW d'96'
        SUBWF Test_Cnt, W
        BTFSC STATUS, Z
        GOTO Threes
        MOVLW d'104'
        SUBWF Test_Cnt, W
        BTFSC STATUS, Z
        GOTO Threes
        MOVLW d'112'
        SUBWF Test_Cnt, W
        BTFSC STATUS, Z
        GOTO Threes
        MOVLW d'120'
        SUBWF Test_Cnt, W
        BTFSC STATUS, Z
        GOTO Threes

        MOVLW d'128'
        SUBWF Test_Cnt, W
        BTFSC STATUS, Z
        GOTO Fours
        MOVLW d'136'
        SUBWF Test_Cnt, W
        BTFSC STATUS, Z
        GOTO Fours
        MOVLW d'144'
        SUBWF Test_Cnt, W
        BTFSC STATUS, Z
        GOTO Fours
        MOVLW d'152'
        SUBWF Test_Cnt, W
        BTFSC STATUS, Z
        GOTO Fours

        MOVLW d'160'
        SUBWF Test_Cnt, W
        BTFSC STATUS, Z
        GOTO Fives
        MOVLW d'168'
        SUBWF Test_Cnt, W
        BTFSC STATUS, Z
        GOTO Fives
        MOVLW d'176'
        SUBWF Test_Cnt, W
        BTFSC STATUS, Z
        GOTO Fives
        MOVLW d'184'
        SUBWF Test_Cnt, W
        BTFSC STATUS, Z
        GOTO Fives

        MOVLW d'192'
        SUBWF Test_Cnt, W
        BTFSC STATUS, Z
        GOTO Sixes
        MOVLW d'200'
        SUBWF Test_Cnt, W
        BTFSC STATUS, Z
        GOTO Sixes
        MOVLW d'208'
        SUBWF Test_Cnt, W
        BTFSC STATUS, Z
        GOTO Sixes
        MOVLW d'216'
        SUBWF Test_Cnt, W
        BTFSC STATUS, Z
        GOTO Sixes

        MOVLW d'224'
        SUBWF Test_Cnt, W
        BTFSC STATUS, Z
        GOTO Sevens
        MOVLW d'232'
        SUBWF Test_Cnt, W
        BTFSC STATUS, Z
        GOTO Sevens
        MOVLW d'240'
        SUBWF Test_Cnt, W
        BTFSC STATUS, Z
        GOTO Sevens
        MOVLW d'248'
        SUBWF Test_Cnt, W
        BTFSC STATUS, Z
        GOTO Sevens

        ;No winner so just display digits
        BCF Test_Cnt, 6
        BTFSS Test_Cnt, 0
        BSF Test_Cnt, 6 ;make sure digits don't match
        MOVFW Test_Cnt
        ANDLW 0x07
        IORLW 0x30
        MOVWF Digit1
        RRF Test_Cnt
        RRF Test_Cnt
        RRF Test_Cnt
        MOVFW Test_Cnt
        ANDLW 0x07
        IORLW 0x30
        MOVWF Digit2
        RRF Test_Cnt
        RRF Test_Cnt
        RRF Test_Cnt
        MOVFW Test_Cnt
        ANDLW 0x07
        IORLW 0x30
        MOVWF Digit3
        GOTO Send_Digs

Zeros MOVLW '0'
        GOTO Winner

Ones MOVLW '1'
        GOTO Winner

Twos MOVLW '2'
        GOTO Winner

Threes MOVLW '3'
        GOTO Winner

Fours MOVLW '4'
        GOTO Winner

Fives MOVLW '5'
        GOTO Winner

Sixes MOVLW '6'
        GOTO Winner

Sevens MOVLW '7'
        GOTO Winner

Winner MOVWF Digit1
        MOVWF Digit2
        MOVWF Digit3
        CALL Send_Digs
        CALL LED_Blink
        CALL LED_Blink
        CALL Msg_On
        CALL LED_Blink
        CALL LED_Blink
        CALL LED_Blink
        CALL LED_Blink
        CALL LED_Blink
        CALL LED_Blink
        CALL LED_Blink
        CALL LED_Blink
        CALL LED_Blink
        CALL LED_Blink
        BSF PORTA, Door ;open the door
        CALL LED_Blink
        CALL LED_Blink
        CALL LED_Blink
        BCF PORTA, Door ;release door solenoid
        CALL Delay1sec
        RETURN

Clickit MOVWF Click_Cnt
clickit1 BSF PORTA, Click
        CALL Delay2ms
        BCF PORTA, Click
        CALL Delay100ms
        DECFSZ Click_Cnt
        GOTO clickit1
        RETURN

Msg_On BSF PORTA, Sound
        NOP
        BCF PORTA, Sound
        RETURN

LED_Blink BSF PORTA, LED1
        CALL Delay200ms
        BCF PORTA, LED1
        BSF PORTA, LED2
        CALL Delay200ms
        BCF PORTA, LED2
        RETURN

;----------------------------------------
; LCD Routines
;----------------------------------------

Init_LCD CALL Delay100ms ;allow LCD time to reset
        MOVLW Cmnd_Mode ;all init done in LCD command mode
        MOVWF Reg_Select
        MOVLW 0x03 ;LCD sees 30 hex
        CALL Cmd_8_Bit
        CALL Delay1ms ;Delay greater than 4.1ms
        CALL Delay1ms
        CALL Delay1ms
        CALL Delay1ms
        CALL Delay100us
        MOVLW 0x03 ;LCD sees 30 hex
        CALL Cmd_8_Bit
        CALL Delay100us ;Delay greater than 100us
        MOVLW 0x03 ;LCD sees 30 hex
        CALL Cmd_8_Bit
        CALL Delay100us ;Delay greater than 100us
        MOVLW 0x02 ;Set 4-bit mode (LCD sees 20 hex)
        CALL Cmd_8_Bit
        CALL Delay100us ;Delay greater than 100us
        MOVLW 0x20 ;Set for 4-bit mode, 16 chars, 1 line
        CALL Write_LCD
        CALL Delay100us ;Delay greater than 100us
        MOVLW 0x01 ;clear display
        CALL Write_LCD
        CALL Delay1ms ;Delay greater than 4 ms
        CALL Delay1ms
        CALL Delay1ms
        CALL Delay1ms
        MOVLW 0x06 ;Entry mode, increment DDRAM, no shift
        CALL Write_LCD
        CALL Delay100us ;Delay greater than 100us
        MOVLW 0x0C ;Display on, cursor off
        CALL Write_LCD
        CALL Delay100us ;Delay greater than 100us
        GOTO No_Digits

Send_Digs CALL No_Digits

        MOVLW Num_Clicks
        CALL Clickit
        MOVLW 0x82
        MOVWF Temp_Adr
        MOVLW ' '
        MOVWF Temp_Dig
        CALL Send_Dig
        MOVLW Num_Clicks
        CALL Clickit
        MOVLW 0x87
        MOVWF Temp_Adr
        MOVLW ' '
        MOVWF Temp_Dig
        CALL Send_Dig
        MOVLW Num_Clicks
        CALL Clickit
        MOVLW 0x8C
        MOVWF Temp_Adr
        MOVLW ' '
        MOVWF Temp_Dig
        CALL Send_Dig

        MOVLW Num_Clicks
        CALL Clickit
        MOVLW 0x82
        MOVWF Temp_Adr
        MOVLW '?'
        MOVWF Temp_Dig
        CALL Send_Dig
        MOVLW Num_Clicks
        CALL Clickit
        MOVLW 0x87
        MOVWF Temp_Adr
        MOVLW '?'
        MOVWF Temp_Dig
        CALL Send_Dig
        MOVLW Num_Clicks
        CALL Clickit
        MOVLW 0x8C
        MOVWF Temp_Adr
        MOVLW '?'
        MOVWF Temp_Dig
        CALL Send_Dig

        MOVLW Num_Clicks
        CALL Clickit
        MOVLW 0x82
        MOVWF Temp_Adr
        MOVLW ' '
        MOVWF Temp_Dig
        CALL Send_Dig
        MOVLW Num_Clicks
        CALL Clickit
        MOVLW 0x87
        MOVWF Temp_Adr
        MOVLW ' '
        MOVWF Temp_Dig
        CALL Send_Dig
        MOVLW Num_Clicks
        CALL Clickit
        MOVLW 0x8C
        MOVWF Temp_Adr
        MOVLW ' '
        MOVWF Temp_Dig
        CALL Send_Dig

        MOVLW Num_Clicks
        CALL Clickit
        MOVLW 0x82
        MOVWF Temp_Adr
        MOVFW Digit1
        MOVWF Temp_Dig
        CALL Send_Dig
        MOVLW Num_Clicks
        CALL Clickit
        MOVLW 0x87
        MOVWF Temp_Adr
        MOVLW '?'
        MOVWF Temp_Dig
        CALL Send_Dig
        MOVLW Num_Clicks
        CALL Clickit
        MOVLW 0x8C
        MOVWF Temp_Adr
        MOVLW '?'
        MOVWF Temp_Dig
        CALL Send_Dig

        MOVLW Num_Clicks
        CALL Clickit
        MOVLW 0x82
        MOVWF Temp_Adr
        MOVFW Digit1
        MOVWF Temp_Dig
        CALL Send_Dig
        MOVLW Num_Clicks
        CALL Clickit
        MOVLW 0x87
        MOVWF Temp_Adr
        MOVLW ' '
        MOVWF Temp_Dig
        CALL Send_Dig
        MOVLW Num_Clicks
        CALL Clickit
        MOVLW 0x8C
        MOVWF Temp_Adr
        MOVLW ' '
        MOVWF Temp_Dig
        CALL Send_Dig

        MOVLW Num_Clicks
        CALL Clickit
        MOVLW 0x82
        MOVWF Temp_Adr
        MOVFW Digit1
        MOVWF Temp_Dig
        CALL Send_Dig
        MOVLW Num_Clicks
        CALL Clickit
        MOVLW 0x87
        MOVWF Temp_Adr
        MOVFW Digit2
        MOVWF Temp_Dig
        CALL Send_Dig
        MOVLW Num_Clicks
        CALL Clickit
        MOVLW 0x8C
        MOVWF Temp_Adr
        MOVLW '?'
        MOVWF Temp_Dig
        CALL Send_Dig

        MOVLW Num_Clicks
        CALL Clickit
        MOVLW 0x82
        MOVWF Temp_Adr
        MOVFW Digit1
        MOVWF Temp_Dig
        CALL Send_Dig
        MOVLW Num_Clicks
        CALL Clickit
        MOVLW 0x87
        MOVWF Temp_Adr
        MOVFW Digit2
        MOVWF Temp_Dig
        CALL Send_Dig
        MOVLW Num_Clicks
        CALL Clickit
        MOVLW 0x8C
        MOVWF Temp_Adr
        MOVLW ' '
        MOVWF Temp_Dig
        CALL Send_Dig

        MOVLW Num_Clicks
        CALL Clickit
        MOVLW 0x82
        MOVWF Temp_Adr
        MOVFW Digit1
        MOVWF Temp_Dig
        CALL Send_Dig
        MOVLW Num_Clicks
        CALL Clickit
        MOVLW 0x87
        MOVWF Temp_Adr
        MOVFW Digit2
        MOVWF Temp_Dig
        CALL Send_Dig
        MOVLW Num_Clicks
        CALL Clickit
        MOVLW 0x8C
        MOVWF Temp_Adr
        MOVFW Digit3
        MOVWF Temp_Dig
        CALL Send_Dig
        RETURN

Send_Dig MOVLW Cmnd_Mode
        MOVWF Reg_Select
        MOVFW Temp_Adr ;write to single address
        CALL Write_LCD
        MOVLW Data_Mode
        MOVWF Reg_Select
        MOVFW Temp_Dig
        CALL Write_LCD
        RETURN

No_Digits MOVLW Cmnd_Mode
        MOVWF Reg_Select
        MOVLW 0x80 ;write at start of line 1 (address 0x00)
        CALL Write_LCD
        MOVLW Data_Mode
        MOVWF Reg_Select
        MOVLW '['
        CALL Write_LCD
        MOVLW ' '
        CALL Write_LCD
        MOVLW '?'
        CALL Write_LCD
        MOVLW ' '
        CALL Write_LCD
        MOVLW ']'
        CALL Write_LCD
        MOVLW '['
        CALL Write_LCD
        MOVLW ' '
        CALL Write_LCD
        MOVLW '?'
        CALL Write_LCD
        MOVLW ' '
        CALL Write_LCD
        MOVLW ']'
        CALL Write_LCD
        MOVLW '['
        CALL Write_LCD
        MOVLW ' '
        CALL Write_LCD
        MOVLW '?'
        CALL Write_LCD
        MOVLW ' '
        CALL Write_LCD
        MOVLW ']'
        CALL Write_LCD
        CALL Delay100ms
        RETURN

Cmd_8_Bit MOVWF PORTC ;byte to write will be in W
        BCF PORTC, Select ;set for command mode
        BSF PORTC, Enable
        NOP
        BCF PORTC, Enable
        RETURN

Write_LCD MOVWF LCD_Data ;byte to write will be in W
        SWAPF LCD_Data, W ;send upper nibble
        ANDLW 0x0F ;clear upper 4 bits of W
        MOVWF PORTC
        BSF PORTC, Select ;preset for data mode
        BTFSS Reg_Select, 0 ;0 = command mode, 1 = data mode
        BCF PORTC, Select ;set for command mode instead
        CALL Delay50us
        BSF PORTC, Enable
        NOP
        BCF PORTC, Enable
        MOVFW LCD_Data ;send lower nibble
        ANDLW 0x0F ;clear upper 4 bits of W
        MOVWF PORTC
        BSF PORTC, Select ;preset for data mode
        BTFSS Reg_Select, 0 ;0 = command mode, 1 = data mode
        BCF PORTC, Select ;set for command mode instead
        BSF PORTC, Enable
        NOP
        BCF PORTC, Enable
        RETURN

;----------------------------------------
; Delay routines (Based on 8-MHz clock)
;----------------------------------------

Delay20us MOVLW d'10'
        GOTO Cntdwn

Delay50us MOVLW d'24'
        GOTO Cntdwn

Delay100us MOVLW d'48'
        GOTO Cntdwn

Delay1ms MOVLW d'249'
        CALL Cntdwn
        MOVLW d'249'
        GOTO Cntdwn

Delay2ms MOVLW d'249'
        CALL Cntdwn
        MOVLW d'249'
        CALL Cntdwn
        MOVLW d'249'
        CALL Cntdwn
        MOVLW d'249'
        GOTO Cntdwn

Delay20ms MOVLW d'20'
        MOVWF Delay_Cnt
loop20ms CALL Delay1ms
        DECFSZ Delay_Cnt, F
        GOTO loop20ms
        RETURN

Delay100ms MOVLW d'100'
        MOVWF Delay_Cnt
loop100ms CALL Delay1ms
        DECFSZ Delay_Cnt, F
        GOTO loop100ms
        RETURN

Delay200ms MOVLW d'200'
        MOVWF Delay_Cnt
loop200ms CALL Delay1ms
        DECFSZ Delay_Cnt, F
        GOTO loop200ms
        RETURN

Delay1sec CALL Delay200ms
        CALL Delay200ms
        CALL Delay200ms
        CALL Delay200ms
        CALL Delay200ms

Cntdwn ADDLW -1 ;decrement W
        BTFSS STATUS, Z ;Zero flag set?
        GOTO Cntdwn ;No, keep looping
        RETURN ;Yes, timeout done

;-------------------------------------------------------------------------------

        END